## Slide 1: NC Division of Coastal Management
NC Department of Environmental Quality
Division of Coastal Management
15A NCAC 07H .0306 Ocean Hazard Area
Cameron Luck
February 27, 2025
Notes: Good Afternoon madame chair and members of the commission. My name is Cameron Luck and I am here to present the staff review of 15A NCAC 07H .0306, which are the General Use Standards for your Ocean Hazard Area

## Slide 2
  At the November 2024 CRC Meeting, the commission identified a portion of 07H .0306 and questioned the Division’s enforcement of that rule.
  Two specific sections of 7H .0306 were discussed:
    07H .0306(e) - Written acknowledgment of the development risks in the Ocean Hazard Area (OHA)
    07H .0306(g) - Permit Condition requiring the dismantling or removal of an imminently threatened structure
15A NCAC 07H .0306 – Review
Notes: At your last CRC meeting, there was some discussion on whether or not portions of the current Ocean Hazard rule are still being utilized or enforced as they are written.
Following that discussion, staff were directed to review .0306 to identify any areas that require attention. Two sections in particular were identified, including 7H .0306(e) and (g), which we will be discussing in more detail here today.

## Slide 3
  CRC rule established the OHA under Section .0300
  OHA encompasses several AECs:
    Ocean Erodible Area
    Inlet Hazard Area
    Unvegetated Beach Area
    State Ports Inlet Management Area
  07H .0306 specifically provides General Use Standards for OHAs
  Objective: regulate development within OHA AECs to ensure any activity or development being proposed aligns with safety and environmental preservation standards of the CAMA.
15A NCAC 07H .0306 – Background
Notes: To provide a quick background on this rule, the Ocean Hazard Area was established under 15A NCAC .0300 in accordance with the Coastal Area Management Act and includes 4 AECs, that occur within the natural hazard areas along the Atlantic Ocean Shoreline. These include the Ocean Erodible Area, the Inlet Hazard Area, the Unvegetated Beach Area, and the State Ports Inlet Management Area.
.0306 provides staff with general use standards for determining permitability of proposed development within these four AECS. These standards include everything from oceanfront setbacks to permitting requirements and are utilized by staff during the permitting process in these areas.
And I just wanted to iterate here that the main objective of your ocean hazard area rules is to ensure any activity or development in these areas aligns with the safety and environmental preservation standards set within the CAMA.

## Slide 4
  15A NCAC 07H .0306(e) requires applicants proposing development within the OHA to “provide written acknowledgment to the Division of Coastal Management indicating the applicant is aware of the risks associated with development in this hazardous area and the limited suitability of this area for permanent structures. The acknowledgement shall state that the Coastal Resources Commission does not guarantee the safety of the development and assumes no liability for future damage to the development.”
  Accomplished through the “Ocean Hazard AEC Notice”
    Informs Property Owner of potential risks they may face when building within OHA
    Provides DCM with signed documentation of this acknowledgment
15A NCAC 07H .0306(e) – Acknowledgement Requirement
Notes: Starting with 07H .0306(e), this section requires property owners to acknowledge they are aware of the risks that come with building within the OHA. This acknowledgement must be written to DCM and should include language that the property owner understands the liabilities and that the CRC does not guarantee the development’s safety.
Currently, this acknowledgement is accomplished through the Ocean Hazard AEC Notice form, which staff provide to the property owner during the permit application period.

## Slide 5
Notes: The form provides the property owner with information specific to their shoreline, including flood water depths, shoreline movement, and current erosion rates, along with preferred protection measures that can be taken should their property become threatened.
On the back of the form is also a brief one-page guide for development along the oceanfront that can be reviewed by the property owner if interested. This is also the only form that must be reviewed and signed by the property owner, not the agent or any other representing party.

## Slide 6
  15A NCAC 07H .0306(e) requires applicants proposing development within the OHA to “provide written acknowledgment to the Division of Coastal Management indicating the applicant is aware of the risks associated with development in this hazardous area and the limited suitability of this area for permanent structures. The acknowledgement shall state that the Coastal Resources Commission does not guarantee the safety of the development and assumes no liability for future damage to the development.”
  Accomplished through the “Ocean Hazard AEC Notice”
    Informs Property Owner of potential risks they may face when building within OHA
    Provides DCM with signed documentation of this acknowledgment
    Form is out of date and would benefit from an update – but serves a valuable purpose.
15A NCAC 07H .0306(e) – Acknowledgement Requirement
Notes: In general, the form is a convenient, simplified document that provides educational information directly into the hands of those considering developing in the OHA while also meeting the current requirements of .0306(e).
Additionally, there is currently no coastal hazards real estate disclosure requirement for buyers, so this form may be the only document required to be signed by the owner acknowledging the coastal hazards present.
However, the form has not been updated for content since 2010 and could use significant revision.

## Slide 7: 15A NCAC 07H .0306(g) – Permit Condition Requirement
  15A NCAC 07H .0306(g) states in part that permits “shall include the condition that any structure shall be relocated or dismantled when it becomes imminently threatened by changes in shoreline configuration as defined in 15A NCAC 07H.0308(a)(2)(B). Any such structure shall be relocated or dismantled within eight years of the time when it becomes imminently threatened, and in any case upon its collapse or subsidence…”
  However, relocating or dismantling of a structure is no longer required if…
  ”…natural shoreline recovery or beach fill takes place within eight years of the time the structure becomes imminently threatened, so that the structure is no longer imminently threatened, then it need not be relocated or dismantled…”
  Sandbags can also be applied for, to provide temporary protections to threatened structures
Notes: Also included on the Ocean Hazard AEC Notice Form is information about the requirement for the removal or relocation of imminently threatened structures. This language is based on 07H .0306(g) which requires a condition to be placed on permits issued within the OHA that details this requirement.
Of the two sections being reviewed by staff, 07H .0306(g) is of particular interest since it is not often applied or enforced. In general, the infrequency of use is a product of the various other solutions available to property owners interested in protecting their property. These include shoreline recover – both through natural processes and beach renourishment. In the memo provided to the CRC, there is an error stating that act of placing sandbags pauses the requirement for the removal or relocation of an imminently threatened structure. The placement of the sandbags does not guarantee a structure is no longer considered imminently threatened but instead offers immediate protection and the property owner an opportunity to potentially promote rapid beach or dune accretion – or explore other options including beach renourishment or even structure relocation.
Even still, the rule is a tool staff want to keep in our enforcement toolbox for when all other protective measures are no longer effective.

## Slide 8: 15A NCAC 07H .0306(e) & (g) – Staff Opinion
  15A NCAC 07H .0306(e) – Acknowledgement Requirement
    Serves as a significant opportunity to educate property owners of potential risks
    Provides DCM with written documentation of acknowledgement
  15A NCAC 07H .0306(g) – Permit Condition Requirement
    Infrequently utilized because alternatives exist for property owners to protect their assets
    Provides DCM with a tool for requiring the removal/relocation of imminently threated structures (once all other options are exhausted)
  At this time, staff are not recommending substantive changes to 15A NCAC 07H .0306.
Notes: Staff believe both .0306(e) and (g) are important sections of .0306 and should be retained.
7H .0306(e) is important because it provides an effective educational mechanism to property owners and gives DCM written documentation that the owner acknowledged the risk of development in an OHA. Staff’s recommendation at this time is for the document to be updated to more accurately reflect current rule.
7H .0306(g) is important because it provides DCM with a useful enforcement tool when all other options for protecting an imminently threatened structure are exhausted. While it is not frequently utilized, when it is needed – it should be available. Therefore, we are not recommending substantive changes to 7H .0306.
As you may have noticed in the submitted Staff memo, a technical change is being proposed that requires your attention. And after additional review, there is actual 2 technical changes for your review.

## Slide 9: 15A NCAC 07H .0306(a)(3) – Technical Change #1
(L) Notwithstanding any other setback requirement of this Subparagraph, replacement of a structure with a total floor area no greater than 10,000 square feet shall be allowed provided that the structure meets the following criteria:
(i) the structure is in a community with an unexpired static line exception, Beach Management Plan approved by the Commission, or was originally constructed prior to August 11, 2009;
(ii) the structure as replaced does not exceed the original footprint or square footage;
(iii) it is not possible for the structure to be rebuilt in a location that meets the ocean hazard setback criteria required under Subparagraph (a)(3) (a)(5) of this Rule;
(iv) the structure as replaced meets the minimum setback required under Part (a)(3)(A) (a)(5)(A) of this Rule; a minimum setback of 60 feet or 30 times the shoreline erosion rate, whichever is greater; and
(v) the structure is rebuilt as far landward on the lot as feasible.
Notes: During the most recent amendments made in 2021/2022, staff overlooked a subparagraph reference that is currently inaccurate and are taking the opportunity to address that issue here. The highlighted portion is the correct citation and should replace the currently incorrect citation.

## Slide 10: 15A NCAC 07H .0306(g) – Technical Change #2
(g) Permits shall include the condition that any structure shall be relocated or dismantled when it becomes imminently threatened by changes in shoreline configuration as defined in 15A NCAC 07H .0308(b)(2)(B)(a)(2)(B). Any such structure shall be relocated or dismantled within eight years of the time when it becomes imminently threatened, and in any case upon its collapse or subsidence. However, if natural shoreline recovery or beach fill takes place within eight years of the time the structure becomes imminently threatened, so that the structure is no longer imminently threatened, then it need not be relocated or dismantled. This permit condition shall not affect the permit holder's right to seek authorization of temporary protective measures allowed pursuant to 15A NCAC 07H .0308(b)(2)(a)(2).
Notes: Similarly, there is currently another inaccurate citation within .0306(g) that needs to be addressed as part of this technical change. This technical change was not included in the included staff memo to the CRC because it was noted after the memo was published on the website. In order to proceed with implementing these two technical changes, CRC must make and approve a motion to do so. Staff would then submit the change to the office of administrative hearings for a history note and update.

## Slide 11
  Questions?