## Slide 1: Transitioning from Construction to Post Construction - Successfully!
Beth McLaughlin
March 2017

## Slide 4: Construction stormwater
Runoff
  TSS: 20,000 to over 160,000 mg/l (McCaleb, et.al., 2008)

## Slide 5: Construction stormwater BMP Treatment Mechanism
  Settling
  Filtering
  Chemical

## Slide 6: Construction stormwater treatment goals
80% TSS reduction
70% settling efficiency for 40 micron particle
Performance based (∆ in turbidity, upstream downstream)
1800 ft3/disturbed acre

## Slide 7: Post construction runoff

## Slide 10: Post construction treatment mechanics
Settle (Storage): Pollutant removal (TSS); peak flow reduction
Infiltration (Soil): Runoff reduction & pollutant removal (all pollutants)
Evapotranspiration (Vegetation): Runoff reduction
Plant Uptake (Vegetation): Pollutant removal (nutrients)
Filtration (Soil and Vegetation): Pollutant removal (TSS, P, N, Metals)
Capture and reuse (all pollutants)
Runoff
Evapotranspiration
Filtration
Underdrain to storm sewer
Infiltration
Filtration
Filtration
Infiltration
Plant Uptake

## Slide 11: Post construction treatment goals
80% TSS reduction
Treat the first 1”
Infiltrate the first 1”
Hydrologic mimickery

## Slide 12: When does construction end and post construction stormwater quality begin?

## Slide 13
How do you transition well without failing your control?

## Slide 14: Post construction stormwater control failure:
Design assumptions
  Soils
9 acres of A soils, but all are very poor for infiltration due to shallow depth to rock (<1’)
Designer

## Slide 15
Wedowee series
Well drained
Moderate permeability
Soil boring
Poor structure
Primarily gray
Low permeability
(holds water far too long!)

## Slide 16: Construction sequencing
Contractor
Regulator
Notes: NCSU – Wilson development included several bioretention cells. Construction stalled during the winter months, sediment clogged the bioretention cells, the contractor couldn’t work on the parking lot because of ponded water and diverted water from another area of the lot to the bioretention area. After the parking lot was completed NCSU extension repaired the bioretention cells by removing the upper 3 inches of soil, planting the cells and stabilizing the banks.

## Slide 17: Compaction
Contractor
Notes: Corn roots in compacted soil (left) and uncompacted soil.

## Slide 18: Compaction reduces infiltration
Treatment goals may not be met
Standing water, vector issues
Poor vegetation health

## Slide 19: Field changes
Improper siting and sizing
Contractor
Regulator

## Slide 20: Overcoming the obstacles….
Notes: Elements include: Permeable pave walk, bioretention swales in ROW, private rain garden subsurface storage chambers under roadway, rain barrels.

## Slide 21
Contractor
Regulator
Designer
Permitee

## Slide 22: Checks and balances
Robust inspection program
Before construction begins – ensure areas for infiltration based BMPs are set aside and marked
During construction – inspect BMP construction; guide sequencing; verify subsurface components
At the end of construction – as-built inspection and engineer certification that treatment goals are met
(I.E., regulations drive the requirements)

## Slide 23: Walk through the perfect design, construction, close out process…

## Slide 24: Designer: Preliminary plan/Concept plan
Understand site constraints and GI opportunities BEFORE site layout
Incorporate step into preliminary plat approval/submission to Planning Dept.
Difficult to set criteria for “better site design”
  Treatment designs do not dictate layout – highlight opportunities in prelim meeting
  Treatment designs do not dictate locations of impervious surface – highlight infiltration areas as “stormwater benefit”
Consider infiltration testing at some level
Appropriateness of BMPs for site

## Slide 25: Final plan
Addresses E&SC as well as post construction
Detailed construction sequence – not simply that construction exists are installed and initial perimeter controls are in place.
Inspector visits site and verifies in field conditions
Check for applicability of BMPs
Approval to install initial measures and call for pre-disturbance inspection
Infiltration tracking through plan requirements
  Concept plan – use soils maps
  Design plans – require infiltration testing in treatment areas
  As-built plan – require infiltration testing to verify treatment is still possible

## Slide 26: Prior to Construction
Regulator has predisturbance meeting on site with designer, contractor and developer
  Designer/developer/contractor - Clearly identify and mark in field areas to be left undisturbed
  Identify areas where compaction is not allowed
  Mark trees to be left
Grading permit/approval is granted and construction begins

## Slide 27: Regulator: Inspections
During construction
  Verify the plan is being followed – but more importantly that the post construction plan is not being failed
  When plan is not followed, require a correction (may need revised E&SC and SW plan)
  Visually verify BMP components – particularly sub surface post construction control elements
  Monitor protection of BMPs and timing of installation

## Slide 28: Construction Observation
Required of design engineer
Verified by inspector
City of Chattanooga

## Slide 29: Inspector and Designer: Prior to CO
Verify as-built BMPs
  Infiltration rates
  Sizes
  Construction materials and techniques
  Vegetation related to GI
Deviations require revision
  Change in the field
  Resubmit SW plan
  As-built details
The final O&M plan

## Slide 30: Designer (and regulator): Final SWMP
Confirm adherence to design standards
Preliminary O&M plan with expectations
Establish the basis against which inspections performed
Construction details
Infiltration testing needed
When infiltration and natural features are included in design, failure to follow the plans could potentially constitute failure to meet the design goals.
  Conservation of natural areas
  Stormwater “sinks”
  Soils
  Buffers

## Slide 31: Regulator and Designer: As-built certification
Required by design engineer at final construction before CO
Verified by inspector
  Verify size
  Verify infiltration rates
Ongoing inspection
Examples:

## Slide 32: Infiltration
At concept, use soils maps
For SWMP, infiltration testing
  Open pit, falling head
  Double ring infiltrometer
Protect infiltration areas during construction from compaction, sediment loading
Nashville: annual verification of infiltration rates (bioretention)

## Slide 33: Checks and Balances
Planning Commission
Other agencies
Engineering Public Works, Stormwater
Register of Deeds

## Slide 34
Montgomery County, MD
Bioretention

## Slide 35: It is possible.
Checks and balances must be in place and monitored by regulator
Detailed construction sequences and plans
Once SW treatment areas are disturbed, potential to have BMP failure is high
Construction observation is critical
Trained inspectors
Revise SWMP when construction negates a BMP