## Slide 1: Department of Environmental Quality
Annette Lucas, PE
What’s New In Stormwater
2017

## Slide 2
The New MDC
The New Design Manual
The New Application Forms
The New Credit Manual

## Slide 3
How the MDC Came to Be…

## Slide 4: 2013 Legislative Mandates
MDC & Fast Track: § 143-214.7B requires DEQ to work with stakeholders to develop Minimum Design Criteria and a Fast-Track Permitting Process.
Rules Review & Re-Adoption: § 150B-21.3A directs state agencies to review and update their rules every 10 years.
Department of Environmental Quality

## Slide 5: The MDC Team
Engineering/design community (8) Home Builder’s Association (1) Construction (1) Local government (4) Environmental Group (2) Landscape Architect (1) Academia (2) Soil Scientist (1) DOT (1) DEQ(4)

## Slide 6: Legislature defines “MDC”
All-inclusive list of requirements for siting, design, construction, and O&M for the fast-track stormwater permitting program.

## Slide 7: MDC to Cover Whole State

## Slide 8: New Lingo!
BMP
-------
SCM
85% TSS Removal
--------------------------
Primary & Secondary SCMs

## Slide 9
WHERE are the MDC?
15A NCAC 2H .1050: MDCs for all SCMs
.1051 through .1062: MDCs for individual SCMs
9
.1052 Bioretention
.1055 SW Wetland
.1051 Infiltration
.1054 Wet Pond
.1058 Permeable Pavement

## Slide 10: Important Dates
The MDC went into effect on January 1, 2017.
Updated Stormwater Design Manual:
Partial draft public posted on 1/4/17
Complete draft on 3/31/17

## Slide 11: How have SCM designs changed?
In general:
Shorter list of requirements
Requirements more objectives-based.
More flexibility & responsibility for designers.
Had to be included in the rules.
Some highlights of the updates . . .

## Slide 12: .1050 General MDC (5) Erosion Protection
Department of Environmental Quality
Inlet(s) and outlet shall be protected from erosion.

## Slide 13: .1050 General MDC (6) Excess Flows
Department of Environmental Quality
Include an overflow device for volumes in excess or the treatment volume or the peak attenuation volume.

## Slide 14: No more level spreaders downslope of wet ponds & infiltration systems!

## Slide 15: .1053 MDC for Wet Ponds
Exclude shelf from average depth calcs.
Vegetated shelf reduced to 6 feet.
2.5*DV
A
A
Forebay
Main Pool
Outlet
DV
Hydraulic Retention Time Method

## Slide 16: .1053 MDC for Wet Ponds
Forebay 15-20% of main pool.
Fountains shall not resuspend sediment or erode side slopes.
Updated vegetation specs.
A trash rack is required.

## Slide 17: .1052 MDC for Infiltration Systems
Shall dewater within 72 hours based on a soil investigation.
No longer require a flow splitting device.

## Slide 18: .1055 MDC for Stormwater Wetlands
Ponding depth increased from 12 to 15 inches.
The first 12” of soil shall be adjusted for plant growth.

## Slide 19: What will happen to the BMP Manual?
North Carolina
Design Manual
Stormwater
Rules = Requirements
Manual = Guidance

## Slide 22: Other Updates
O&M-EZ
Supplement-EZ
Also, we’re working on on-line application forms for projects under DEQ’s authority.

## Slide 23: Supplement-EZ

## Slide 24
Explain why SCMs were classified primary v. secondary.
Update our SCM credits based on current research.
Consistent between all NC SW programs.
Credit Manual

## Slide 25: Primary SCM
From 2H .1002:
A wet pond, SW wetland, infiltration system, sand filter, bioretention cell, permeable pavement, green roof, rainwater harvesting, or an approved new stormwater technology that is in accordance with the MDC.
Can stand alone when designed per the MDC to treat the design storm depth.

## Slide 26: Secondary SCM
From 2H .1002:
An SCM that does not achieve the annual reduction of TSS of a Primary SCM but can be used in a treatment train with a primary SCM to provide pre-treatment or hydraulic benefits.
May not stand alone; must be used with another SCM.

## Slide 27
Primary SCMs | Secondary SCMs
Wet Pond Stormwater Wetland Infiltration System Sand Filter Bioretention Cell Permeable Pavement Rainwater Harvesting Green Roof | DIS LS-FS Pollutant Removal Swale Dry Pond

## Slide 28: Explanation
WHY don’t we say
85% TSS removal
any more?
Because it’s wrong!

## Slide 29
SCM Performance per Research

## Slide 30
Chart: Influent Conc of TSS (mg/L)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120 | 125 | 130 | 135 | 140 | 145 | 150 | 155 | 160
 | 14.2 | 17.75 | 21.3 | 24.85 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 25 | 26.25 | 27.5 | 28.75 | 30 | 31.25 | 32.5 | 33.75 | 35 | 36.25 | 37.5 | 38.75 | 40
Test Not Valid
29%
25 mg/L
75%
Standards for Primary SCMs
Primary
Secondary

## Slide 31: Options in New Rules
Runoff treatment: SW from all of the built-upon area is treated in primary SCMs or a combo of Primary and Secondary SCMs that provides equal or better treatment. (one Drainage Area, one Primary SCM)
Runoff volume match (aka LID): the annual runoff volume after development does is not more than 10% higher than the amount annual runoff volume before development. (5% in SA waters)

## Slide 32: Runoff Volume Match: More Complicated!
For SCMs we need to know:
How much SW is treated versus untreated?
Of the treated SW, how much is effluent v. ET&I?
SW into SCM
Treated Runoff
Untreated Runoff
Effluent
ET&I

## Slide 33: Fates of Treated Runoff:
Effluent
Treated discharge from an SCM
ET&I
Infiltration, ET, Harvest

## Slide 35
SCMs (designed per the MDC unless otherwise specified) | % of annual runoff treated if 100% sized
Infiltration Permeable Pavement Wet Pond Stormwater Wetland Dry Pond | 84%
Bioretention | 94%
Sand Filter (open or closed) StormFilter | 90%
LS-FS DIS Pollutant Removal Swale | 90%
Rainwater Harvesting | 85%

## Slide 36
SW into SCM (on an annual basis)
Treated Runoff
Untreated Runoff
Effluent
ET&I
Infiltration Permeable Pavement Wet Pond Stormwater Wetland Dry Pond | 84%

## Slide 37: Size V. Runoff Treated
84%

## Slide 38
SCMs (designed per the MDC unless otherwise specified) | % of annual runoff treated if 100% sized
Infiltration Permeable Pavement Wet Pond Stormwater Wetland Dry Pond | 84%
Bioretention | 94%
Sand Filter (open or closed) StormFilter | 91%
LS-FS DIS Pollutant Removal Swale | 90%
Rainwater Harvesting | 85%

## Slide 39: Sizing versus Runoff Fates for Infiltration Systems
100% Sizing
70% Sizing
130% Sizing

## Slide 40: What if I can’t remember all of this?
This is all programmed into the Jordan Falls tool!
Storm-EZ needs to be updated….
A goal for 2017 will be to finish the “SNAP” tool that will do both nutrient and LID calculations

## Slide 41: Questions?
Department of Environmental Quality