## Slide 1: Units Conversion
There are 1,000 milligrams (mg) in 1 gram (g)
  milli = 1 *10-3
  milligrams per liter (mg/l) are equal to parts per million (ppm)
There are 1,000,000 micrograms (ug) in 1 gram
  micro = 1 x 10-6
  micrograms per liter (ug/l) are equal to parts per billion (ppb)
There are a 1,000,000,000 nanograms in 1 gram
  nano = 1 x 10-9
  nanograms per liter (ng/l) are equal to parts per trillion

## Slide 2: Units Conversion (cont)
1,000 ug in 1 mg
1,000,000,ng in 1 mg
1,000 ng in 1 ug
Or look at it backwards
0.001 mg in 1 ug
0.000001 mg in 1 ng
0.001 ug in 1 ng

## Slide 3: Units Conversion (cont)
I’ll never remember all that !
grams >> milligrams >> micrograms >> nanograms
Move 3 decimal places between each
Bigger to smaller decimal moves right
Smaller to bigger decimal moves left

## Slide 4: Examples
Convert 32.1 ug/l (ppb) to mg/l (ppm)
32.1 ug/l
3.21 one
0.321 two
0.0321 three
0.0321 mg/l

## Slide 5: Examples
Convert 0.000056 mg/l (ppm) to ng/l (ppt)
0.000056 mg/l
0.00056 one
0.0056 two
0.056 three
That gets us to ug/l
0.056 ug/l

## Slide 6: Examples
Convert 0.000056 mg/l (ppm) to ng/l (ppt)
0.056 ug/l
0.56 one
5.6 two
56.0 three
Now we are at ng/l!
56 ng/l

## Slide 7: Tip
I always remember mercury:
0.0002 mg/l = 0.2 ug/l = 200 ng/l

## Slide 8: A side note
“milli” comes from the Latin for thousand. So how
come mg/l is called “part per million”? It has do to
with the fact that the term “parts per million” is a
weight to weight ratio. A liter of water weighs
Approximately 1,000 grams or 1,000,000 mg. Thus
one mg/l is equal to 1 ppm.

## Slide 9: Concentration Analogies
One-Part-Per-Million (ppm or mg/L)
  one automobile in bumper-to-bumper traffic from Cleveland to San Francisco
  one inch in 16 miles
  one minute in two years
  one ounce in 32 tons
  one cent in $10,000

## Slide 10: Concentration Analogies cont.
One-Part-Per-Billion (ppb or ug/L)
  one 4-inch hamburger in a chain of hamburgers circling the earth at the equator 2.5 times
  one silver dollar in a roll of silver dollars stretching from Detroit to Salt Lake City
  one kernel of corn in a 45-foot high, 16-foot diameter silo
  one sheet in a roll of toilet paper stretching from New York to London
  one second of time in 32 years

## Slide 11: Concentration Analogies cont.
One-Part-Per-Trillion (ppt or ng/L)
  one square foot of floor tile on a kitchen floor the size of Indiana
  one drop of detergent in enough dishwater to fill a string of railroad tank cars ten miles long
  one square inch in 250 square miles
  one mile on a 2-month journey at the speed of light