## Slide 1
NCDEQ Stormwater Program: NPDES MS4 Permitting
February 2020

## Slide 2
Department of Environmental Quality
What is Stormwater?
NPDES MS4 Program
NPDES MS4 Permits
Compliance Initiative
Tools & Resources
Presentation Overview

## Slide 3: What is Stormwater & Why is it a Problem?
Department of Environmental Quality
Storm events produce runoff (stormwater)
Runoff washes pollutants off of land surfaces
Runoff is not treated at the wastewater facility
Stormwater runoff carries harmful pollutants directly into our local creeks and waterways
Pollutants increase downstream drinking water treatment costs and impair recreational uses
Aquatic life and vegetation are sensitive to pollutants

## Slide 4: Federal NPDES MS4 Program
National Pollutant Discharge Elimination System (NPDES)
  Federal Clean Water Act Permitting Program for:
    Wastewater Permits
    Stormwater Permits (40 CFR 122)
Municipal Separate Storm Sewer System (MS4)
  MS4 is a system of conveyances to collect and transport stormwater runoff
  NPDES MS4 Permits are for discharges of stormwater to surface waters from a publicly owned/operated stormwater collection system

## Slide 5: North Carolina NPDES MS4 Program
Department of Environmental Quality
EPA Oversight & Delegation to NCDEQ
NCDEQ Program Implementation
  Permitting
  Customer Support
  Compliance Audits
  Enforcement *
  Reporting to EPA
  * EPA can also enforce in addition to NCDEQ

## Slide 6: North Carolina NPDES MS4 Program
Department of Environmental Quality
1990’s: 6 Phase I MS4s + NCDOT
2000’s: 115 Phase II Permittees
2023ish: New Designations
2025ish: New Permittees Apply
Tentative Schedule for New MS4 Designations

## Slide 7
Department of Environmental Quality
Federal Designation into the NPDES MS4 Program
US Census Urbanized Area
Population >50,000
Fringe cluster of 2,500 – 50,000
Regulated MS4s represent 4% of the US land area and >80% of the population.

## Slide 8
Department of Environmental Quality
State Designation (15A NCAC 02H.0151)
Potential for Adverse Water Quality
Population/Density/Housing Units
Petitions
State Designation into the NPDES MS4 Program

## Slide 9
Department of Environmental Quality
Urbanized Area <1,000 people
  Not contributing pollutant loadings to a regulated MS4
  No WLA under a TMDL (A different Clean Water Act program, see next slide)
Small MS4 <10,000 people
  DEQ has evaluated all your receiving waters (unlikely)
  No WLA under a TMDL
  No potential for significant water quality impacts (unlikely)
NPDES MS4 Program Waivers

## Slide 10
TMDLs & WLAs: The Only Time You Don’t Want Pie!
A TMDL is the whole pie.
A WLA is the slices of pie.
Total Maximum Daily Load (TMDL)
The total amount of a pollutant that a specific waterbody can handle.
Waste Load Allocation (WLA)
How much each primary source of the pollutant can contribute to the water body.

## Slide 11
Department of Environmental Quality
Fund the Stormwater Management Program
Implement a Comprehensive Stormwater Management Plan (SWMP)
Document Program Implementation
Report Annually
Obtain a New Permit Every 5 Years
Six Minimum Control Measures / Program Areas
NPDES MS4 Permit Requirements

## Slide 12
  Public Education & Outreach
  Public Involvement & Participation
  Illicit Discharge Detection & Elimination (IDDE)
  Construction Site Runoff Controls
  Post-Construction Site Runoff Controls (PC)
  Pollution Prevention & Good Housekeeping for Municipal Operations (PP/GH)
Six Required Minimum Control Measures
Image by City of South Portland

## Slide 13
Department of Environmental Quality
Pollution Prevention & Good Housekeeping for:
Municipal “Industrial” Facilities (and maybe a general stormwater permit too!)
Spill Response
MS4 (collection system) O&M
O&M of Municipal Stormwater Control Measures (SCMs)
Pesticide, Herbicide & Fertilizer Management
Vehicle & Equipment Maintenance
Pavement Management
PP/GH: Minimum Control Measure #6

## Slide 14
Department of Environmental Quality
Goal 1: An Efficient & Compliant MS4 Program
  Restructured DEQ’s MS4 Program
  Created an Informative Web Page
  Standardized Tools & Processes
  Provided Outreach, Training & Technical Support
  Published a 5-Year Audit Schedule
  Compliant MS4s
  Happy EPA
Image by msdresponsibility.com
EPA / NCDEQ MS4 Compliance Initiative
  2020
  2018

## Slide 15
Department of Environmental Quality
COMPLIANCE
DON’T WANT TO TAKE ADVANTAGE OF THIS ONE-TIME OFFER?
3rd permit term = mandatory compliance
Maximum civil penalty is $37,500 per day for each violation.
Maximum criminal penalty is $25,000 per day of violation and/or 1 year imprisonment.
GET ANOTHER 5 YEARS TO COME INTO COMPLIANCE!
EPA / NCDEQ MS4 Compliance Initiative

## Slide 16
Department of Environmental Quality
Notice of Compliance (NOC) | Notice of Deficiency (NOD) | Notice of Violation (NOV)
3 | 3 | 24
Image by Redbubble
** Plus ANOTHER 5 pending a decision **
MS4 Compliance Audit Outcomes (Through Feb. 2020)

## Slide 17
  Lack of Documentation
    If you can’t prove it, it didn’t happen!
  Incomplete MS4 Mapping
    All major outfalls should already be mapped!
  Reactive Illicit Discharge Programs
    MS4s are required to proactively find and eliminate illicit discharges!
Top 3 Compliance Deficiencies
Image by Smartsheet.com

## Slide 18
Department of Environmental Quality
A NOC is issued to MS4s that have nothing or just a few small things to fix
The NOC requires the permittee to do 2 things:
Submit a Draft Stormwater Management Plan (SWMP) (120 days)
Submit a permit renewal application once DEQ & MS4 concur on the Draft SWMP (30 days)
Notice of Compliance (NOC)

## Slide 19
Department of Environmental Quality
A NOD is issued to MS4s that have several little things or one big thing to fix.
The NOD is a NOC + 2 additional things:
Submit a written response to the Notice (30 days)
Conduct a self-audit of whatever DEQ didn’t audit (120 days)
Submit a Draft SWMP (120 days)
Submit a permit renewal application once DEQ & MS4 concur on the Draft SWMP(30 days)
Notice of Deficiency (NOD)

## Slide 20
Department of Environmental Quality
Notice of Violation (NOV)
A NOV is issued to MS4s that have major issues with their program.
The NOV is a NOD + 1 more thing:
Submit a written response to the Notice (30 days)
Adopt a Council Resolution demonstrating support for a compliant stormwater program (60 days)
Conduct a self-audit of whatever DEQ didn’t audit (120 days)
Submit a Draft SWMP (120 days)
Submit a permit renewal application once DEQ & MS4 concur on the Draft SWMP (30 days)

## Slide 21
  Acknowledgement that the city/town:
  Is in it’s 3rd permit term
  Received a Notice of Violation (NOV) from NCDEQ
  Must comply with the NOV & permit requirements
  Is required to provide adequate program funding and staffing
  Will receive enforcement penalties for not complying with the NOV
  Could also be subject to enforcement by EPA
NOV: Council Resolution Requirements
Image by timescall.com

## Slide 22
Department of Environmental Quality
Receipt of NOV
30
Submit Written Response to NOV
60
Submit Council Resolution
120
DAYS
30
Submit
Self-Audit & Draft SWMP
Submit Permit Application & Draft SWMP
Written Concurrence on Draft SWMP
MS4
DEQ
Notice of Violation (NOV) Timeline

## Slide 23
MS4 Permit Renewal Process

## Slide 24
Department of Environmental Quality
NCDEQ Stormwater Web Page:
www.deq.nc.gov/sw
DEMLR Stormwater Laserfiche Repository: https://edocs.deq.nc.gov/WaterResources/
MS4 Program Contact:
Jeanette Powell (919) 707-3620 jeanette.powell@ncdenr.gov
NCDEQ MS4 Tools & Resources