## Slide 1: Department of Environmental Quality
Overview of Subpart K

## Slide 2: Credit
Original Presentation created by
Environmental Protection Agency
Office of Resource Conservation and Recovery (ORCR)
And adapted by NCDEQ, Division of Waste Management
Hazardous Waste Section

## Slide 3: What is Subpart K?
40 CFR 262 Subpart K
Alternative Requirements for Hazardous Waste Determination and Accumulation of Unwanted Material for Laboratories Owned by Eligible Academic Entities
"Academic Laboratory Rule" or "Labs Rule"
Notes: For LQGs and SQGs, Subpart K provides alternative requirements for waste determination (262.11) and satellite accumulation (262.15) in laboratories owned by eligible academic entities that choose to be subject to this subpart.
For VSQG, Subpart K provides alternative requirements to the conditional exemption in 262.14 (VSQG requirements) for the accumulation of hazardous waste in laboratories owned by eligible academic entities that choose to be subject to this subpart.

## Slide 4: What will be covered?
Basics of the Labs Rule
Rationale for the Labs Rule
Main Provisions of the Labs Rule

## Slide 5: Overview
Rule effective on federal level December 31, 2008
North Carolina fully adopted rule April 1, 2010
Rules found at 40 CFR 262 Subpart K
Notification required to opt in (electronically using myRCRAInfo)
This rule is optional, but if an eligible entity opts into, all applicable requirements must be met
Notes: Subpart K is an optional rule for eligible academic entities
Eligible academic entities can choose to comply with existing regulations or Subpart K

## Slide 6: Who is Eligible?
Applicable to eligible academic laboratories that generate hazardous waste
Who is "eligible"?
Colleges & Universities
Non-profit research institutes and teaching hospitals owned by or with formal written affiliation agreement with a college or university
Notes: The lab can generate LQG, SQG or VSQG amounts of hazardous waste and still be eligible

## Slide 7: Who is not Eligible?
Not applicable to:
Commercial research & development labs
Government facilities
Non-teaching hospitals
Non-profit research facilities and teaching hospitals not owned by nor have formal written affiliation with a college or university
High school laboratories

## Slide 8: Benefits of Opting Into Subpart K?
Provides flexibility to make hazardous waste determinations:
In the laboratory
At an on-site central accumulation area
  SQG and LQG only, does not apply to VSQG
At an on-site treatment, storage, or disposal facility
  SQG and LQG only, does not apply to VSQG
Provides incentives to clean-out old and expired chemicals that may pose unnecessary risk
Notes:   Labs typically operate under the satellite accumulation area (SAA) regulations of 40 CFR 262.15
  Subpart K provides alternate RCRA generator regulations for managing hazardous waste in academic labs for SQG and LQG

## Slide 9: Hazardous Waste at Academic Laboratories
Requires development of Laboratory Management Plan (LMP)
Safer laboratory practices
Increased awareness of hazardous waste management
Eligible academic entities may choose to remain subject to the pre-existing hazardous waste generator requirements and not opt in to Subpart K
Notes: Subpart K is an optional rule for eligible academic entities
  Eligible academic entities can choose to comply with existing regulations or Subpart K

## Slide 10: Hazardous Waste at Academic Laboratories
For more information:
Rule summary, rule history, additional resources:
https://www.epa.gov/hwgenerators/managing-hazardous-waste-academic-laboratories-rulemaking
https://www.epa.gov/hwgenerators/regulations-hazardous-waste-generated-academic-laboratories
https://deq.nc.gov/about/divisions/waste-management/hw/technical-assistance-education-guidance/documents

## Slide 11: Rationale for the Academic Labs Rule
Teaching & Research Labs vs. Industry Labs:
Hazardous waste generation pattern is different
  Lots of different wastes streams that vary over time
  Small amounts of each hazardous waste
  Many individuals generating hazardous waste in many labs
Often, Students, generate the hazardous waste
  High turnover (thus difficult to train)
  Lack the expertise & accountability of a professional workforce

## Slide 12: Rationale for the Academic Labs Rule
Hazardous waste generation pattern
+ Student presence
Very difficult to make
accurate HW determinations
at the point of generation

## Slide 13: Rationale for the Academic Labs Rule
Solution:
Require trained professionals to make the HW determination instead of students
Allow HW determination to be made after initial point of generation
Any material in the laboratory that has the potential to be HW is managed as HW in the laboratory

## Slide 14: Applicability of the Two Regulatory Provisions
Satellite Accumulation Area (SAA)
Applies to SQGs and LQGs
Applies to any SQG or LQG that chooses to establish an SAA “at or near the point of generation”
Laboratory
Applies to VSQGs, SQGs and LQGs
Applies only to labs at an "eligible academic entity" that opts into Subpart K:
  College or University (C/U)
  Teaching Hospital that is owned by or has a formal written affiliation agreement with a C/U
  Non-profit Research Institute that is owned by or has a formal written affiliation agreement with a C/U
Satellite Accumulation Area
Subpart K

## Slide 15: Terminology of the Two Regulatory Provisions
Hazardous Waste (HW)
Acute Hazardous Waste
(124 P-listed chemicals with 1quart liquid/1 kg solid HW threshold in SAA)
"Unwanted Material" OR
other "equally effective term" that you choose
Reactive Acutely Hazardous Unwanted Material
  (6 P-listed chemicals with 1 qt threshold in lab)
Satellite Accumulation Area
Subpart K

## Slide 16: What is considered a Subpart K "Laboratory"?
What is a Laboratory*? | YES | NO
Teaching & research labs Art studios Photo labs Field labs Diagnostic labs in teaching hospitals Areas that support labs (e.g., chemical stockrooms & prep rooms) |  | 
Chemical stockrooms that do not support labs Vehicle maintenance areas Machine shops Print shops Commercial photo processing Power plants |  | 












* Laboratories must be OWNED by the eligible academic entity and must not be used for production.

## Slide 17: Notification
SQGs and LQGs must notify that they are generating HW but do not have to specify that they are accumulating HW in an SAA
Eligible Academic Entity must notify Hazardous Waste Section that it is opting into Subpart K
  Use the Site ID Form (electronically using myRCRAid) to notify
  Site ID Form includes option to opt-in to Subpart K
  Can withdraw from Subpart K using myRCRAid
All laboratories at an EPA ID # (or site) must opt in together
Satellite Accumulation Area
Subpart K

## Slide 18
The old paper version of the 8700-12 form.
Page 5, #12
Subpart K – Academic Labs Opt in or Withdraw
Notes: If an eligible academic entity is opting into Subpart K, then they should check box A and indicate what type of entity they are. More than one can apply.
If an eligible academic entity is withdrawing from Subpart K, then they should check box B.

## Slide 20: myRCRAid
Questions about myRCRAid?
Nivia Webb
Phone: 919-707-8229
Email: Nivia.Webb@ncdenr.gov
Now facilities will enter facility information directly into the RCRAInfo database instead of submitting a hard copy form for entry
Link to a brief summary about registering for myRCRAid and further information on a tutorial for myRCRAid:
  https://files.nc.gov/ncdeq/Waste%20Management/DWM/HW/
  Electronic%20Filing%20of%20EPA%20Notifications.pdf

## Slide 21: Electronic myRCRAid looks similar to the paper 8700-12 Form

## Slide 22: Electronic myRCRAid looks similar to the paper 8700-12 Form

## Slide 23: Electronic myRCRAid looks similar to paper 8700-12 Form

## Slide 24: Questions about myRCRAid?
Nivia Webb
Phone: 919-707-8229
Email: Nivia.Webb@ncdenr.gov

## Slide 25: Container Labeling
Containers of HW must be marked/labeled with the words
  "Hazardous Waste" and
  Indication of the hazards of the contents of the container
Containers of Unwanted Materials must be labeled with:
  The words "Unwanted Materials" or another "equally effective term" used consistently and
  Information to alert emergency responders to the contents of the container (e.g., name of chemical) and
  Information sufficient to make a hazardous waste determination and
  Accumulation start date
Satellite Accumulation Area
Subpart K
“Affixed or
Attached
To” Label
“Associated with” Label
May be “affixed or attached” if preferred
Notes: Because the HW determination is not made at the exact time as the point of generation, the container labeling must provide sufficient information to allow a HW determination to be
made at a later time

## Slide 26: Container Labeling Terminology
What does "Affixed or Attached to" label mean?
Label must be physically connected to, and not be separated from, the container
  Examples:
  Sticker on the bottle of unwanted material
  Label attached to bottle with wire or tape (reminder-securely attached)
What does "Associated With" label mean?
  Labeling system that allows you to track information back to a specific container such as:
  Spreadsheet
  Log Book
  Barcoding
"Associated with" labels do not have to be physically with the containers
Information can be stored electronically

## Slide 27: Examples of "Affixed or Attached to" Labels

## Slide 28: Example of "Associated With" Label
"Affixed or Attached to" Label
that corresponds with the "Associated with" label to the right

## Slide 29: Container Labeling for Subpart K
Often, the label in use in your SAA area may be used and modified slightly to work for Subpart K labeling
  The following slides include example labels that colleges and universities are currently using
Examples demonstrate the flexibility of the two types of labeling:
  Label "affixed or attached to" the container
  Label "associated with" the container
Examples are illustrative only and are not meant to be exhaustive

## Slide 30: Container Labeling for Subpart K
The following slides show 3 container label examples for unwanted materials that are non-halogenated solvents that would be listed hazardous waste when the hazardous waste determination is made
Container labels for unwanted materials that are halogenated solvents can be done in a very similar way
Key to making a HW determination and assigning proper HW codes - need to know whether solvent has been spent or not

## Slide 31: Example Label for Unwanted Materials
This example was provided by Connecticut University.

## Slide 32: Example Label for Unwanted Materials
This example was provided by the University of Washington.

## Slide 33: Example Label for Unwanted Materials

## Slide 34: Container Labeling Examples
The following slides show two container label examples for unwanted materials that would be determined to be:
Characteristic hazardous waste
Non-hazardous waste (which are also unwanted materials while in the laboratory)

## Slide 35: Example Label for Unwanted Materials
This example was provided by Clark University.

## Slide 36: Example Label for Unwanted Materials
This example was provided by Harvard University.

## Slide 37: Container Labeling Examples
Example Labels from Clean-out
Containers of unwanted materials from a once-per-12 month laboratory clean-out are labeled
  According to the same labeling requirements as all other containers of unwanted materials in the laboratory
    This way there is one labeling system in the laboratory
May want to add information on the label to identify containers from a laboratory clean-out, especially if they are moved to a central accumulation area
A label distinguishing laboratory clean-out containers will provide needed information on what to count toward generator status
The following two examples are for unused unwanted materials from a laboratory clean-out

## Slide 38: Example Label for Unwanted Materials
This example was provided by Ursinus College.

## Slide 39: Example Label for Unwanted Materials
This example was provided by Cornell University.

## Slide 40: Labeling Tips
Look at labels currently used - may be able to change the words "Hazardous Waste" and use the same labels
When you choose what to call unwanted materials, think about how it will help you separate unwanted materials from the laboratory (regulated under Subpart K) from hazardous waste generated elsewhere on campus (regulated under satellite accumulation area and standard generator regulations)
You may want to include a check box on your label to distinguish between used and unused unwanted materials

## Slide 41: Labeling Tips
You may want to design additional labels or fields for
Working containers
Laboratory clean-out waste
If you have a central accumulation area (90 or 180-day area), you may want to make a label for your containers of unwanted material that can be adapted easily once the containers have been transported to the hazardous waste central accumulation area
Remember once your container arrives at the central accumulation area it must be dated according to the SQG and LQG generator regulations
Remember that within 4 days of arriving in the central accumulation area, the words “Hazardous Waste” must be added to a container of unwanted material that is a hazardous waste to indicate that the initial hazardous waste determination has been made

## Slide 42: Container Management
Containers must be in good condition
Contents must be compatible with container
Containers must be kept closed except:
  When adding, removing , or consolidating HW; or
  When temporary venting of the container is necessary
    For proper operation of equipment, or
    To prevent dangerous situations, such as a build-up of pressure
Containers must be in good condition
Contents must be compatible with container
Containers must be kept closed except:
  When adding, removing, or bulking unwanted materials
  Working container* may be open until end of procedure or shift, whichever is first
  When venting of a container is necessary
    For operation of equipment such as HPLCs
    To avoid pressure build-up
Satellite Accumulation Area
Subpart K
* Working container ≤ 2 gallons

## Slide 43: Training
No training of SAA personnel is required
Training required for personnel outside SAA
  Must have standard RCRA generator training, pursuant to their generator status
  No CAA at VSQGs, so no training required
Training that is "commensurate with duties" is required for all laboratory personnel which includes:
  Laboratory workers, and
  Students
Training required for personnel outside lab (trained professionals)
  Must have standard RCRA generator training, pursuant to their generator status
  Trained professional at VSQGs must train to SQG standards
Satellite Accumulation Area
Subpart K

## Slide 44: Removing HW from the Laboratory
Volume-driven removals of HW from SAA:
  3 days to remove the excess of 55 gallons of hazardous waste, if 55 gallons of HW (or 1 quart/1 kg acute HW) is exceeded
Time-driven removals of unwanted materials from laboratory:
  All containers must be removed from the lab at a regular interval not to exceed 12 months, or
  Rolling 12 months: each container must be removed within 12 months from the container’s accumulation start date
AND
Volume-driven removals of unwanted materials from lab:
  10 days to remove unwanted materials if 55 gallons (or 1 quart/1 kg of acute reactives) is exceeded
Satellite Accumulation Area
Subpart K

## Slide 45
In the SAA:
Acute Hazardous Waste
  124 P-listed chemicals (unused commercial chemical products)
  6 F-listed wastes
  If 1quart liquid acute HW or
  1 kg solid acute HW is exceeded in SAA, must be removed within 3 days
Generator status for facility: all 124 P-listed chemicals have 1 kg/month threshold that triggers LQG status
In the lab:
Reactive Acutely Hazardous Unwanted Material
  6 reactive P-listed chemicals (unused commercial chemical products)
  P006 – Aluminum phosphide
  P009 – Ammonium picrate
  P065 – Mercury fulminate
  P081 - Nitroglycerine
  P112 - Tetranitromethane
  P122 – Zinc phosphide (> 10%)
If 1 quart of liquid or 1 kg of solid is exceeded in lab, must be removed within 10 calendar days
Generator status for facility: all 124 P-listed chemicals have 1 kg/month threshold that triggers LQG status
Satellite Accumulation Area
Subpart K
Acute Waste in the Laboratory

## Slide 46
Generator must make HW determination at the point of generation
  The time and place HW is first generated
Individuals generating the HW generally make the initial HW determination
Eligible Academic Entity (LQG and SQG) may choose when and where to make HW determination:
  In laboratory (but after the time of initial HW generation), or
  Within 4 calendar days of arriving at an on-site:
    Central accumulation area or
    Interim status or permitted treatment, storage, or disposal facility (TSDF)
Individuals making the HW determination must be “trained professionals”
Satellite Accumulation Area
Subpart K
Hazardous Waste Determination
For LQG and SQG Facilities
Notes: 46

## Slide 47
Generator must make HW determination at the point of generation
  The time and place HW is first generated
Individuals generating the HW generally make the initial HW determination
Eligible Academic Entity (VSQG) must make the waste determination in the laboratory (but can be after the time of initial HW generation)
Individuals making the HW determination must be “trained professionals”
VSQG Facilities
Subpart K
Hazardous Waste Determination
For VSQG Facilities
Notes: 47

## Slide 48
Trained professional must accompany all unwanted material that is transferred from the laboratory(ies) to the CAA
Must date the container when it arrives at CAA, which starts the
  4-day clock for HW determination
  90-day or 180-day clock for accumulation time
Unwanted material becomes subject to applicable LQG/SQG generator rules when it arrives at CAA except for the labeling requirements
Subpart K
Waste Determination in CAA
For LQG and SQG Facilities

## Slide 49
If it is a HW, must add the words "Hazardous Waste" and an indication of the hazards of the contents of the containers within 4 days of arrival at CAA
  Can mark/label the “affixed or attached to” container label
Can delay adding the HW code until immediately prior to off-site shipment
  Can mark/label "affixed or attached to" label or "associated with" label
Subpart K
Waste Determination in CAA
For LQG and SQG Facilities (continued)

## Slide 50
The point of generation remains the same, only the hazardous waste determination is delayed
All unwanted materials are managed as hazardous waste in the laboratory until the hazardous waste determination is made
Unwanted materials in the laboratory will likely include materials that turn out to be non-hazardous wastes once the hazardous waste determination is made
Count the HW toward the eligible academic entity's generator category in the calendar month that the HW determination was made
Subpart K
Hazardous Waste Determination

## Slide 51
Containers may NOT be transferred between SAAs, therefore on-site consolidation may ONLY occur in a
  Satellite accumulation area
  Central accumulation area
Containers MAY be transferred between laboratories, therefore on-site consolidation MAY occur in a
  Laboratory or
  In a central accumulation area
Consolidation laboratory
  Same time limits on how long containers can remain in the laboratory (i.e., 12 months)
  Same volume limits on how much unwanted material is allowed in the laboratory
  Only trained professionals can transfer the containers outside the lab
Satellite Accumulation Area
Subpart K
On-Site Consolidation
Transferring Containers Outside the SAA/Lab

## Slide 52
No provision for a generator to consolidate HW at an off-site location, unless the receiving facility is:
  An interim status or permitted TSDF or
  A transfer facility
Satellite Accumulation Area
Subpart K
No provision for a generator to consolidate HW at an off-site location, unless the receiving facility is:
  An interim status or permitted TSDF or
  A transfer facility
Off-Site Consolidation

## Slide 53
No incentives to conduct
laboratory clean-outs are
provided:
  If exceed 55 gallons of HW, must remove the excess within 3 days
  All HW generated in a laboratory clean-out must be counted toward generator status
  Laboratory clean-outs will often increase generator status (e.g. from SQG to LQG)
Regulatory incentives to
conduct laboratory clean-out
are provided:
  Laboratory clean-out waste has no volume limit--must remove all laboratory clean-out waste after 30 days
  HW generated during a laboratory clean-out that is unused commercial chemical product does not have to be counted toward generator status
  Incentives can be used one time per laboratory per 12 months
Satellite Accumulation Area
Subpart K
Laboratory Clean-Out Incentives

## Slide 54
Laboratory clean-outs are not mandatory
30-day clock for clean-out begins when you start sorting through cabinets and taking inventory
At the end of 30 days, all laboratory clean-out unwanted materials must be removed from the laboratory and
  Sent to on-site CAA or on-site TSDF, or
  Sent off-site for disposal
Subpart K
Laboratory Clean-Out Details

## Slide 55
On-site Management of laboratory clean-out waste
  Unused commercial chemical products are not counted toward generator status
  VSQGs and SQGs will not have increased regulatory burden because of a laboratory clean-out
Off-site Management of laboratory clean-out waste
  If weight of laboratory clean-out waste makes the eligible academic entity exceed the VSQG monthly limits, then all HW must be managed and disposed of as HW when sent off-site
    >1 kg of acute HW or
    >100 kg of HW
Subpart K
Laboratory Clean-Out Details

## Slide 56
Manifesting laboratory clean-out waste
  Use Box 14 on the manifest titled, “Special Handling Instructions and Additional Information”
  Indicate that a portion or all the waste on the manifest is from a Subpart K laboratory clean-out
Documentation laboratory clean-out waste
  Identify laboratory being cleaned out,
  Date the clean-out begins and ends, and
  Volume of HW generated during laboratory clean out
  Keep documentation 3 years from date of clean-out
Subpart K
Laboratory Clean-Out Details

## Slide 57
Squeaky Clean University (SCU) is a normally a VSQG
Squeaky Clean University conducts a laboratory clean-out:
  Generates 5 kg P-listed acute HW (unused commercial chemical products)
  This amount is >1 kg of acute HW/month weight limit for VSQGs
  Normally, SCU would become an LQG for the month
  But, SCU does not count the 5 kg of unused commercial chemical product towards generator status
Laboratory Clean-Out Example
Subpart K

## Slide 58
  SCU remains a VSQG for purposes of on-site accumulation
    SCU does not have to meet LQG requirements (biennial reporting, contingency plans, documented training)
  For off-site management, since the VSQG limits have been exceeded, all HW must be managed as HW when sent off-site (e.g., manifested, LDRs, TSDF, etc.)
Laboratory Clean-Out Example (continued)
Subpart K

## Slide 59
LMP is not required
Two-part LMP is required
Contents of Part I are enforceable
  Two Elements:
    Identify options for container labeling
    Identify option for regular removal of unwanted material from laboratories
Contents of Part II are not enforceable
  Seven Elements
    Best intended practices for laboratory HW management
Satellite Accumulation Area
Subpart K
Laboratory Management Plan (LMP)

## Slide 60
Must implement and comply with two specific provisions in Part I of LMP:
Describe procedure for container labeling
  Identify whether the term "unwanted material" will be used on the containers in the laboratory
    If "unwanted material" is not used, identify the equality effective term that will be used that has the same meaning (must be used consistently and is subject to the same requirements as the term "unwanted material")
  Identify the manner in which information that is "associated with the container" will be imparted
Laboratory Management Plan (LMP)
Part I, Two Elements
Notes: Procedure for container labeling as described in 40 CFR 262.206(a)

## Slide 61
Must implement and comply with two specific provisions of Part I of LMP:
Identify whether the regularly scheduled unwanted material removal of containers from each laboratory will occur:
  On a regular interval, not to exceed 12 months or
  Within 12 months of each container's accumulation start date
Laboratory Management Plan (LMP)
Part I, Two Elements
Notes: Procedure for container labeling as described in 40 CFR 262.206(a)

## Slide 62
Description of intended Best Practices for:
Container labeling & management
Providing training for laboratory workers & students commensurate with duties
Providing training to ensure safe on-site transfers of unwanted material and HW by trained professionals
Removing unwanted material from laboratory
  Regularly scheduled removals
  When the maximum volumes are exceeded
Laboratory Management Plan (LMP)
Part II, Seven Elements

## Slide 63
Description of intended Best Practices for:
Making HW determinations, specifying duties of the individual involved with the process
Laboratory clean-outs, if eligible academic entity plans to use the incentives for laboratory clean-outs, including:
  Procedures for conducting laboratory clean-outs
  Procedures for documenting laboratory clean-outs
Laboratory Management Plan (LMP)
Part II, Seven Elements (continued)

## Slide 64
Description of intended Best Practices for:
Emergency prevention, including:
  Procedures for emergency prevention, notification, and response appropriate to the hazards in the laboratory
  A list of chemicals the eligible academic entity has, or is likely to have, that become more dangerous when they exceed their expiration date and/or they degrade
  Procedures to safely dispose of chemicals that become more dangerous
  Procedures for timely characterization of unknowns
Laboratory Management Plan (LMP)
Part II, Seven Elements (continued)

## Slide 65
Contents of Part I of LMP are Enforceable
  Can be held in violation if your practices vary from the LMP procedures you develop
Contents of Part II of LMP are Not Enforceable
  Can NOT be held in violation if your practices vary from the LMP procedures you develop
Can be held in violation if all 9 required elements are not reasonably addressed in your LMP
Laboratory Management Plan (LMP)

## Slide 66
One LMP covers ALL laboratories at an EPA ID # (or site) that opts in
If you have multiple EPA ID #’s (or sites) that opt in
  One LMP may cover multiple sites
LMP may be incorporated into another plan
  For example: OSHA’s Chemical Hygiene Plan
LMP includes procedures many have already developed
Laboratory Management Plan (LMP)

## Slide 67
Laboratory clean-outs must be documented
  Identify laboratory cleaned out
  Start and end date of laboratory clean-out
  Volume of laboratory clean-out hazardous waste
Training records must be kept by LQGs for
  Laboratory workers (but not for students)
  Trained professionals (as required by existing generator regulations)
Subpart K
Recordkeeping

## Slide 68
If unwanted material does not meet the definition of a solid waste (in 40 CFR 261.2) it is no longer subject to Subpart K (or the RCRA HW rules)
If unwanted material does not meet the definition of a hazardous waste (in 40 CFR 261.3), it is no longer subject to Subpart K (or the RCRA HW rules)
Subpart K
Unwanted Material that is not Solid or HW

## Slide 69: Questions?