## Slide 1: Mercury Minimization Plans
Deborah Gore
PERCS Unit
December 17, 2013
Notes: Many of you were at the Consortium meeting in March and heard most of this then, but I am going to give you just a little bit of background on the TMDL, the permitting strategy and the requirements of the mercury minimization plans. There were some edits made to the plan after the comments received at the meeting in March and I’ll point those out in particular.

## Slide 2: Background
Statewide TMDL for HG
  Statewide fish consumption advisory
67% reduction from 2002 baseline
The waters have moved to Category 4
2% of Hg from point sources
NPDES wastewater portion is 81 pounds/year
Notes: The DWR has issued a statewide total maximum daily load (or TMDL) in response to a statewide fish consumption advisory for mercury. The TMDL calls for a 67% reduction in mercury levels from all sources from the year 2002 baseline mercury loading. We used 2002 as the baseline year to get credit for the reductions that have been achieved since the Clean Smokestack Act of 6/2002.
The TMDL was approved by EPA in October 2012 and the waters were delisted and moved to category 4. Category 4 waters are also considered impaired but already have an EPA approved TMDL. The fish consumption advisory won’t be lifted until fish tissues data suggest so. DWR doesn’t do that, DHHS does so I’m not sure of how that works. The TMDL shows that when all sources meet the 67% reduction then the fish tissue data should meet the mercury target. That means the whole world has to reduce Hg emissions by 67% before the mercury target for fish tissue is expected to be met.
About 2% of the mercury in the waters come from point sources. The other 98% comes from atmospheric deposition. We only contribute about 16% of the mercury found in NC waters.
The NPDES wastewater share of the TMDL is 81 pounds/year. The actual wastewater loading was 252 pounds in 2002. It is believed that we are currently well under the 81 lbs of Hg per year. Believe we will meet the target for nonpoint sources by 2016.

## Slide 3: Permitting Strategy
Technology Based Effluent Limits (TBELs)
TBEL Level Currently Achieved (LCA)
  98.5% below 47 ng/l
  93% can regularly comply
Permitted design capacity of more than 2 MGD
Monitoring only if
  All averages are less than 12 ng/l
  No single value over 47 ng/l
  In conjunction with priority pollutant analysis
  Develop MMP if Hg at quantifiable levels
Notes: In general, the Reasonable Potential Analysis is used to decide if a NPDES permit should contain a particular effluent limit. The effluent limits are then set using Water Quality Based Effluent Limits [dividing the WQS by the IWC] or Technology Based Effluent Limits. TBELs seemed most appropriate in this case.
All of the mercury monitoring data for the past 5 years was evaluated to establish a level that is currently achieved by WWTPs in NC. 98.5% of all the data was less than 47 ng/l and 93% of facilities with mercury monitoring or limits can regularly comply with this limit without any new treatment technology.
MMPs will only be required at WWTPs with a design capacity of more than 2 MGD and mercury at quantifiable levels in their effluent
The permit writers will calculate the annual average mercury concentrations for each of the past 5 years. If all of the averages are less than the current WQS of 12ng/l and no single daily value is greater than the LCA of 47 ng/l, the permit will have a monitoring only requirement. This takes into account the upstream mercury concentration. If you have an IWC of 50% and the WQS is 12 ng/l, then you can have 24 ng/l at your effluent. But if we have data showing the upstream mercury is 6 ng/l then we have to subtract that out and you can only have 18 ng/l. If we don’t have data we can assume 0 upstream.
The monitoring will be required in conjunction with the priority pollutant analysis and MMP identifying contributors and goals for reduction IF there is mercury at quantifiable levels in the effluent.

## Slide 4: Edit to Permitting Strategy
(2) Consistently detectable levels of mercury in their effluent.
Suggested revision
; with “consistently” being defined as equal to or greater the 75%... and “detectable” being defined as greater than ½ of the current WQS…
Notes: The original document required the MMP at facilities with greater than 2 MGD design capacity and consistently detectable levels of mercury in their effluent.
It was suggested that it be revised to define consistently as being detections in 75% or more of the effluent samples and detectable being greater than ½ of the current WQS. Which would be greater than 6 ng/l.
Unfortunately, the TMDL approved by EPA requires the MMP at facilities with mercury in the effluent and really does not give us the flexibility to use these definitions. This is the only suggestion that we were not able to accommodate.

## Slide 5: Permitting Strategy 2
Major facilities with Hg limit
  Monitor quarterly
  Develop MMP
  Will be the more stringent of TBEL vs. WQBEL
  Annual average concentration
  AA < 12 ng/l & none >47 ng/l, limit removed
Major facilities receiving a new Hg limit
  4 years to develop and start implementing MMP
  Limit assigned in 5th year of permit
Notes: Major facilities with a Hg limit will be required to monitor quarterly – reduction from weekly.
Will have to develop a MMP identifying contributors and goals for reduction. The MMP must be developed within 180 days after the permit is issued.
If the limit calculated based on the current water quality standard of 12 ng/l is less than the Level Currently Achievable you will get the WQ based limit. If the limit calculated based on the current water quality standard is greater than the LCA, the limit will be 47 ng/l. The limit will be an annual average concentration. No one will get a limit greater than 47 ng/l.
If you currently have a limit and the annual averages are less then 12 ng/l and no single data point above 47 ng/l, the limit will be removed upon renewal.
If this will be a new limit than you have 4 years to develop and implement the MMP and in the 5th year of the permit the limit will be assigned. The MMP will still need to be developed in 180 days and you will have the next 3.5 years to implement it and hopefully by the time the limit comes into effect you will be able to comply with the limit

## Slide 6: Permitting Strategy cont.
New/Expanding facilities
  Allowed as long as aggregate point source load not exceeded
Minor facilities
  Monitor 1/5 years
Special Cases
  Instream concentrations > 12ng/
  Limits > 47 ng/l
Notes: New and expanding facilities will be allowed as long as the overall aggregate point source load is not exceeded. They will have to develop MMP if they have consistent detectable mercury in the effluent. If there is reasonable potential then there will be a limit assigned as described in previous slide.
So if you are at a greater than 2 MGD WWTP, and unless you have data that is mostly <1ng/l, you will have to develop and implement a MMP. You may not have a limit, so you’ll have less monitoring, but the MMP will still be required.
Minor facilities will be required to monitor once/5 years and a limit will be assigned if data suggests one is needed. If
you have a pretreatment program you are considered a major plant and if you are at a 2 MGD or less WWTP you will probably be sampling more often than once in 5 years, due to the priority pollutant scan and your pretreatment monitoring plan, but unless the data shows that you need a limit, you will not get one or have to do a MMP. If a limit is assigned a MMP is required.
Case-by-case permit limit decisions will be made for dischargers into streams with instream sampling data greater than 12 ng/l to determine if that discharger is a contributor to the instream mercury load.
Permit limits above 47 ng/l may be assigned in case where DWr determines that achievement of the LCA is technically infeasible or economically unreasonable. The statewide aggregate loading will not be exceeded.

## Slide 7: Model Mercury Minimization Plan
Typically focus on pretreatment controls
  Non-domestic users
  General public
  http://portal.ncdenr.org/web/wq/swp/ps/npdes
Section I – Purpose
  Reduce amount of Hg discharged to system
  Guide the utility in its efforts
Section II – Facility Description
  Treatment process & record (as warranted)
Notes: Typically MMPs focus on pretreatment controls on non-domestic users and outreach to the general public regarding the proper use and disposal of mercury containing household products. It focuses on BMPs. The MMPs are intended to be a reasonable, low-cost approach to managing the 2% load from point sources.
There is a model on the NPDES web site.
The first section is the purpose. Of course we are trying to reduce the amount of mercury that gets into the system and the MMP is a guide for the utility to do that through BMPs. The MMP may also help control some of the Hg reaching the storm sewer system.
In Section II, there’s a place to enter information regarding your treatment process and treatment record. This is a model and not all information is required but remember this is a way you can tell the Public about the efforts you may have already made to reduce mercury and toxic pollutants in general.
Then there is some generic language about how WWTPs are not designed to treat for mercury and that mercury is not used at the plant but comes form sources such as industrial users, laboratories, other businesses, residual mercury deposits from past practices, trace amounts from household products and atmospheric deposition. And you may have information about how well your WWTP does remove mercury.

## Slide 8: Model Mercury Minimization Plan 2
Section III – Program Plan
  Non-domestic sources
    Assess data for non-domestic users
    Survey other common sources
    Ask IUs to review process chemicals
    Updated every 2 5 years
  Additional Control Measures
    Pollution Prevention
    Housekeeping, Spill Control, Education
    Public Outreach
Notes: You have 180 days, or about 6 months, to develop the MMP and then within 2 years of that the POTW must evaluate available information to assess the potential for non-domestic users to contribute mercury. Some of the things you may look at include influent and effluent data, industrial user monitoring data, TRIs, State Hazardous site registry, National Priority list and historical record of industrial sites. This is one other minor edit – it previously said you WILL look at all of these, now it’s more of a list of suggested items that may be useful to review.
You must also survey other common sources of Hg like dental offices, hospitals, labs, auto recyclers and any other potential sources based on existing information. Ask the IUs to review process chemical and show that Hg concentrations are below industry average. Request replacement of chemicals containing high amounts of Hg. This evaluation must be updated every 5 years – which was revised from 2 years.
You also want to do some pollution prevention at your plant by substituting any Hg containing treatment chemicals. At one time sodium hydroxide was a common source for mercury in treatment plant chemicals.
You will have to develop procedures to minimize the possibility of any spills of mercury containing substances at the WWTP and add mercury identification and proper disposal to operator training.
The Public outreach part requires information on sources and proper use and disposal of household mercury be posted on the town web site and mailings to customers periodically to point it out. Facilitate public awareness of collection programs for mercury containing products

## Slide 9: Model Mercury Minimization Plan 3
  Additional Control Measures (cont)
    Waste Management Practices
    Laboratory practices
  Tracking and monitoring
    Inspect Survey annually
    Track and report on program
    Monitor influent at least annually; require IUs to monitor
    Measure effluent Hg as required by NPDES permit or pretreatment monitoring plan
Notes: The waste management section was sort of a pledge to help other governmental entities to educate the public on programs to recycle and properly dispose of things like spent fluorescent bulbs, batteries and other mercury containing products. But is has been taken completely out of the model plan – it depended on the cooperation of other entities for success so was not really a fair requirement because it was not in your control.
If you have a lab then this part is a pledge to train employees in proper handling and disposal of mercury containing compounds and replacing mercury thermometers where practical.
There has to be some way to measure the success of the program so beginning after the first full year after the MMP is implemented you will survey, notice it did say INPSECT, at least 10% of any non-domestic users that were id’d as possible significant sources of mercury; track the implementation of the program; monitor the influent mercury at least annually and require significant non-domestic sources of mercury to periodically monitor; measure the effluent Hg as per the NPDES permit, or your pretreatment monitoring plan, whichever is more.
You will notice that “and report” has been deleted. It didn’t have a time frame for reporting and there is a reporting requirement in the last section.

## Slide 10: Model Mercury Minimization Plan 4
Section IV - Implementation of Control Measures
  What you have already done
Section V - Annual Report Reporting
  Available on web site
  Information on non-domestic users
  Summarize public outreach
  Summarize the implementation efforts
  Influent monitoring trends
  Any adjustments to the Plan
  Summarize MMP activities as part of NPDES renewal
Notes: In Section IV you get to tell about what you have already done to minimize mercury. Obviously, all of you have implemented a local pt program, you may have developed local limits for mercury, implemented collection and proper disposal of mercury containing equipment.
The last part of the Plan the Reporting requirement. Initially there was to be an annual reporting requirement, but that seemed to be overkill, so it was cut back to a summary of the activities submitted with your NPDES permit renewal.

## Slide 11: More information
http://portal.ncdenr.org/web/wq/ps/mtu/tmdl/tmdls/mercury
Notes: More info on TMDL. This link is imbedded in the first page of the Model MMP.