## Slide 1
April 11, 2019
NPDES MS4 Phase II
Total Maximum Daily Load (TMDL) and
Watershed Planning

## Slide 2: Different Scenarios …
Department of Environmental Quality
One | Two | Three | Four
Water not meeting water quality standards | Water not meeting water quality standards | Water not meeting water quality standards | Water meeting water quality standards
TMDL developed | TMDL developed | No TMDL developed | NA
TMDL/WLA reqs in MS4 permit | No TMDL/WLA reqs in MS4 permit | No TMDL/WLA reqs in MS4 permit | NA
Notes: 82 days

## Slide 3: NPDES MS4 Phase II Permit Requirements
Department of Environmental Quality
Public Education & Outreach
Public Participation & Involvement
Illicit Discharge Detection & Elimination (IDDE)
Construction Site Runoff Controls
Post-Construction Runoff Controls (PC)
Pollution Prevention/Good Housekeeping (PP/GH)
Develop a comprehensive Stormwater Management Plan (SWMP)
to address six Minimum Control Measures (MCMs):
…and sometimes TMDLs
Notes: 82 days

## Slide 4: Questions and Answers about Total Maximum Daily Load???
Department of Environmental Quality
What is a TMDL?
Total Maximum Daily Load or …
Calculation of maximum amount of pollutant that water can receive and still meet water quality standards.
What is a pollutant?
Substance in the environment in certain quantities that has undesired effects, or adversely affects the usefulness of a resource
Example
Money Creek can handle up to 1 lb/day of Nickel and still meet water quality standards (10 g/L to meet aquatic life).
More information on some of these items … stay tuned .
Notes: 82 days

## Slide 5: Why do we have to deal with TMDLs?
Department of Environmental Quality
TMDL Program is a Federal program authorized under the Clean Water Act to address waters that are not meeting water quality standards. EPA requires TMDLs (or alternative) to be done for waters not meeting water quality standards.
Notes: 82 days

## Slide 6: When does TMDL apply to MS4???
Department of Environmental Quality
Permitted MS4
discharges in water(s)/watershed(s)
with approved TMDL(s)
Notes: 82 days

## Slide 7: Is MS4 in watershed with approved TMDL?
Department of Environmental Quality
See TMDL map to determine if MS4 falls within watersheds covered by TMDL https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=bc125c8b5ccf4110b538db1188731690
Notes: 82 days

## Slide 8: Why does my stream/watershed have a TMDL?
Department of Environmental Quality
MS4 discharge(s) into water(s) is/are not meeting water quality standards for one or more parameters (pollutants)
And
TMDL has been developed (States have 8-13 years to develop TMDL after it is determined water not meeting standards)
Notes: 82 days

## Slide 9: Is/Are receiving water(s) meeting standards???
Department of Environmental Quality
Is receiving water meeting water quality standards?
Check 2014 Integrated Report
https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=dcb44280272e4ac49d9a86b999939fec
2018 Draft Integrated Report map
https://ncdenr.maps.arcgis.com/apps/MapSeries/index.html?appid=14df5075d8e3437b8476c89c3db3f0a5
(overlay MS4 stormwater map with this map, if possible)
Notes: 82 days

## Slide 10: What do you mean “water not meeting standards?”
Department of Environmental Quality
Water Uses, Classifications and Standards .. NC is required to …
Assess water(s), land uses, etc. to determine use(s) (i.e., water supply),
Develop classification(s) associated with use(s) (i.e, WSII)
Develop standards to protect uses associated with classifications (i.e, nitrate nitrogen 10mg/l).
Use | Classification | Standard
Drinking Water | Water Supply II (WSII) | Nitrate Nitrogen 10 mg/l
Notes: 82 days

## Slide 11: How do we know if water – not meeting standards?
Department of Environmental Quality
Water Monitoring and Assessment
Physical/Chemical Monitoring – Monthly – Regional Offices
Biological Monitoring – every five years – central office
Special Studies – frequency varies
Notes: 82 days

## Slide 12: Questions and Answers about Total Maximum Daily Load???
Department of Environmental Quality
What is a TMDL?
Total Maximum Daily Load or …
Calculation of maximum amount of pollutant that water can receive and still meet water quality standards.
What is a pollutant?
Substance in the environment in certain quantities that has undesired effects, or adversely affects the usefulness of a resource
Example
Money Creek can handle up to 1 lb/day of Nickel and still meet water quality standards (10 g/L to meet aquatic life).
Notes: 82 days

## Slide 13: Different Scenarios …
Department of Environmental Quality
One | Two | Three | Four
Water not meeting water quality standards | Water not meeting water quality standards | Water not meeting water quality standards | Water meeting water quality standards
TMDL developed | TMDL developed | No TMDL developed | NA
TMDL/WLA reqs in MS4 permit | No TMDL/WLA reqs in MS4 permit | No TMDL/WLA reqs in MS4 permit | NA
Notes: 82 days

## Slide 14: Scenarios One and Two: MS4 Permit - TMDL Requirements
Department of Environmental Quality
If permit has stormwater Waste Load Allocation (WLA) requirements from TMDL, comply with requirements,
OR …
If permit has no stormwater WLA requirements from TMDL, for six MCMs, evaluate strategies and revise BMPs to enhance water quality recovery strategies in watershed.
Within 12, 24, 36 months of TMDL approval …
- different documentation requirements
Notes: 82 days

## Slide 15: Scenarios One and Two: How do I learn more about TMDL for receiving water(s) into which my MS4 discharges?
Department of Environmental Quality
See map with MS4s that fall within watersheds covered by TMDL https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=bc125c8b5ccf4110b538db1188731690
Notes: 82 days

## Slide 16: Scenario One or Two: TMDL info
Department of Environmental Quality
Water Name | Assessment Unit | Water Quality Classification (uses) | Parameter not meeting standards | Length (miles)
Haw River | 16-(1)d | C – aquatic life and secondary recreation | turbidity | 13
Pollutant (tons/day) | Existing Load | TMDL | Percent (%) Reduction | WLA | LA
TSS | 183 | 71 | 61 | 22 | 49
Pollutant (tons/day) | Existing Load | Wastewater | Stormwater
TSS | 22 | 13 | 9
Notes: 82 days

## Slide 17: Scenarios One and Two: MS4 Permit - TMDL Requirements
Department of Environmental Quality
If permit has stormwater Waste Load Allocation (WLA) requirements from TMDL, comply with requirements,
OR …
If permit has no stormwater WLA requirements from TMDL, for six MCMs, evaluate strategies and revise BMPs to enhance water quality recovery strategies in watershed.
Within 12, 24, 36 months of TMDL approval …
- different documentation requirements
Notes: 82 days

## Slide 18: How to meet permit and/or address water quality problems in your MS4 and/or watershed?
Department of Environmental Quality
Use MS4 Permit and Stormwater Management Plan – Six Minimum Measures (Revise, Improve, etc)
– Scenarios One and Two
Develop Watershed Plan?
- Scenarios One, Two, Three or Four
Nine Element
Six Element (4b) – waive TMDL?
Source Water Protection Plan
????
Notes: 82 days

## Slide 19: Before developing a watershed plan, check …
Department of Environmental Quality
Has watershed plan already been done?
Check Use Restoration Watershed map
https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=09324bbee06a4546ad175f238f8a4ea6
Check 319 map
https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=c2461274b3ff4009a8c405c4bddeb3aa
If plan has been done,
- Learn about plan and see how MS4 can be a part of implementing this plan, offer ways to improve plan???
If plan has not been done, see next slide …
Notes: 82 days

## Slide 20: When to develop Watershed Plan???
Department of Environmental Quality
Develop watershed plan if …
A strong local entity within watershed that has interest and ability/resources to develop and help implement the plan (i.e., nonprofit, cooperative extension, etc.)
Watershed boundaries are similar to MS4 boundaries
Notes: 82 days

## Slide 21: Why develop Watershed Plan???
Department of Environmental Quality
Organized path forward
Structure around which to gather support and resources
MS4 already meeting several requirements of watershed plan by implementing program
Obtain grant funding
Notes: 82 days

## Slide 22: EPA 319 Nine Element Watershed Plan Requirements
Department of Environmental Quality
When developing EPA 319 watershed plan, it must meet following requirements:
1. Identification of Causes and Sources of Impairment (target pollutants, other concerns and their sources)
2. Proposed management measures to address pollutants
3. Expected load reductions from proposed management measures
4. Technical and Financial Assistance Needs
5. Information, Education and Public Participation
6. Schedule for Implementing Management Measures
7. Interim Milestones for Implementation
8. Criteria for Determining Load Reductions and Water Quality Improvement
9. Water Quality Monitoring/Load Reduction
Notes: 82 days

## Slide 23: EPA 319 Nine Element Watershed Plan Requirements (continued)
Department of Environmental Quality
Plans must be developed for water/watershed(s) not meeting water quality standards and must meet nine elements
Plans must be submitted/approved to be eligible for monies
Monies only used for plan implementation
Monies CANNOT be used to implement MS4 permit requirements, but can be used to develop/implement management measures NOT in permit, but still helping improve water quality.
Notes: 82 days

## Slide 24: Why develop watershed plan … different scenarios …
Department of Environmental Quality
One | Two | Three | Four
Water not meeting water quality standards | Water not meeting water quality standards | Water not meeting water quality standards | Water meeting water quality standards
TMDL developed | TMDL developed | No TMDL developed (a) | NA
TMDL permit reqs | No TMDL permit reqs | No TMDL permit reqs | NA
Eligible for 319 funds if develop watershed plan (WSP) | Eligible for 319 funds if develop watershed plan (WSP) | Eligible for 319 funds if develop watershed plan (WSP) | Not eligible for 319 funds
Use 319 monies for management measures NOT in permit | Use 319 monies for management measures NOT in permit (more flexibility) | 319 monies used for management measures NOT in permit (most flexibility) | 
(a) WSP could allow for TMDL delay or exemption
Notes: 82 days

## Slide 25: Different Scenarios (continued) – Scenario Three
Department of Environmental Quality
Scenario Three: Water not meeting standards and no TMDL developed
If watershed plan meets certain requirements, TMDL development may be delayed or waived
Watershed plan demonstrates how water quality improvement and restoration will be achieved
Little Alamance Creek (4b Six Element Plan)
https://files.nc.gov/ncdeq/Water%20Quality/Planning/TMDL/Alternatives/Little%20Alamance/Little_Alamance_4b_Report_Final_Dec2014.pdf
Notes: 82 days

## Slide 26: Why develop watershed plan … different scenarios …
Department of Environmental Quality
(a) WSP could allow for TMDL delay or exemption
One | Two | Three | Four
Water not meeting water quality standards | Water not meeting water quality standards | Water not meeting water quality standards | Water meeting water quality standards
TMDL developed | TMDL developed | No TMDL developed (a) | NA
TMDL permit reqs | No TMDL permit reqs | No TMDL permit reqs | NA
Eligible for Water Resources Development Grant or see other funding? | Eligible for Water Resources Development Grant or see other funding? | Eligible for Water Resources Development Grant or see other funding? | Eligible for Water Resources Development Grant or see other funding?
Notes: 82 days

## Slide 27: Interesting Points to Consider (continued) ….
Department of Environmental Quality
Other funding sources (such as Water Resources Development Grant) to help improve water quality in your MS4 jurisdiction, watershed … please see
https://deq.nc.gov/about/divisions/water-resources/planning/basin-planning/use-restoration-watershed-programs/funding
Notes: 82 days

## Slide 28: Resources summary …
Department of Environmental Quality
Funding resources https://deq.nc.gov/about/divisions/water-resources/planning/basin-planning/use-restoration-watershed-programs/funding
TMDL resources https://deq.nc.gov/about/divisions/water-resources/planning/modeling-assessment/tmdls
Watershed plan resources https://deq.nc.gov/about/divisions/water-resources/planning/basin-planning/use-restoration-watershed-programs
Water Quality Data Assessment resources
2014 Integrated Report - https://ncdenr.maps.arcgis.com/apps/webappviewer/index.html?id=dcb44280272e4ac49d9a86b999939fec
2018 Draft Integrated Report map
https://ncdenr.maps.arcgis.com/apps/MapSeries/index.html?appid=14df5075d8e3437b8476c89c3db3f0a5
Notes: 82 days

## Slide 29: Paul Clark Water Supply Watershed Protection Program Coordinator (919) 707-3642 paul.clark@ncdenr.gov
From the right point of view, every storm and every drop in it is a rainbow.
-Henry David Thoreau