## Slide 1: DSCA PFAS Pilot Study Overview
Delonda Alexander, NCDEQ
Special Remediation Branch Head

## Slide 2: Introduction
  Florida Department of Environmental Protection (FDEP) conducted a limited study in 2019 that indicated that polyfluoroalkyl substances (PFAS) can be associated with the waste streams of dry cleaners
  To evaluate whether PFAS contamination poses a significant concern at sites in NC, the Dry-Cleaning Solvent Cleanup Act (DSCA) Program will conduct limited sampling for PFAS at selected sites as part of a pilot study
  NCGS 143-215.104N(a)(7) authorizes fund expenditures for “other activities reasonably required to protect public health and the environment” – these expenditures are being made at a certified facility pursuant to an assessment and remediation agreement

## Slide 3: Site Selection
  10-15 existing DSCA sites will be selected
  Sites will represent a range of facility types including:
    Active vs. historical operations
    With and without wet-wash laundry operations
    At least one solvent distribution/wholesale facility
  Sites will represent range of conditions including:
    Different geology and hydrogeology
    Variable chlorinated solvent concentrations
    At least one petroleum solvent release site
  Will avoid sites in Bladen, Brunswick, Colombus, Cumberland, New Hanover, Pender, Robeson and Sampson counties that are associated with GenX/PFAS contamination

## Slide 4: Sampling Approach for Each Site
  Minimum of 2 groundwater samples will be collected during one sampling event
  One sample from an upgradient monitoring well and one sample from the well exhibiting the highest solvent concentration
  Quality Assurance/Quality Control (QA/QC) samples will be collected including an equipment blank and a field blank
  Samples will be analyzed by an accredited laboratory using EPA Method 1633 for 40 specific PFAS compounds
  Results compared to various standards including EPA maximum contaminant levels (MCLs), NC Interim Maximum Allowable Concentrations (IMACs) and the lab quantitation limit

## Slide 5: DEQ PFAS Signature Tool
  A tool for evaluating PFAS signatures which can help to identify potential sources
  Based upon PFAS source, there are different signatures, including long-chain and short-chain carbon compounds
  The tool provides a pie chart of the PFAS signature based upon compounds detected
  PFAS signatures can be compared across samples to see patterns or lack of similarity

## Slide 6: DEQ PFAS Signature Tool - Example

## Slide 8
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
Chart: 
9
1
7
2
3
4
5
6
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 0 | 0 | 0 | 0 | 0.35 | 0 | 0 | 0 | 0 | 0 | 0.22 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 1.5 | 0.39 | 1.1 | 0 | 1.6 | 0 | 0 | 0 | 197 | 849 | 342 | 253 | 9 | 1.4 | 0 | 0 | 0 | 0 | 0 | 0 | 17.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 8.4 | 0.53 | 4.8 | 0 | 0 | 0 | 0 | 0 | 819 | 2880 | 1660 | 1080 | 201 | 0 | 0 | 1.2 | 0 | 0 | 0 | 0 | 9.4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 0 | 0 | 0 | 0 | 0.39 | 0 | 0 | 0 | 1.9 | 0.35 | 0 | 0.45 | 0.85 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
 | 0.4 | 0 | 0.3 | 0 | 1.3 | 0 | 0 | 0 | 9.2 | 8.8 | 6.3 | 3.8 | 4.9 | 2.9 | 0.38 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 2.1 | 0 | 0 | 0 | 0.45 | 0 | 0 | 0 | 0 | 0.34 | 0 | 0 | 0.37 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 0.48 | 0 | 0.39 | 0 | 0.72 | 0 | 0 | 0 | 1.9 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.66 | 0.97 | 0.53 | 0.31 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 0.41 | 0.307 | 1.04 | 0 | 3.05 | 0 | 0 | 0 | 0 | 1.4 | 1.33 | 0.633 | 2.57 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 0.603 | 0.52 | 2.26 | 0 | 5.06 | 0 | 0 | 0 | 1.02 | 3.78 | 3.4 | 1.3 | 5.27 | 0.224 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| PFBS | PFPeS | PFHxS | PFHpS | PFOS | PFNS | PFDS | PFDoS | PFBA | PFPeA | PFHxA | PFHpA | PFOA | PFNA | PFDA | PFUnA | PFDoA | PFTrDA | PFTeDA | 4:2 FTS | 6:2 FTS | 8:2 FTS | PFOSA | NMeFOSA | NEtFOSA | NMeFOSAA | NEtFOSAA | NMeFOSE | NEtFOSE | HFPO-DA (GenX) | ADONA | PFMPA | PFMBA | NFDHA | 9CI-PF3ONS | 11CI-PF3OUdS | PFEESA | 3:3 FTCA | 5:3 FTCA | 7:3 FTCA
Well 1 | 0 | 0 | 0.274 | 0 | 0.478 | 0 | 0 | 0 | 0 | 0.333 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Signatures: Source and Receptor (Parcels)
Receptors
Source
1/17/24
Total PFAS
  MW 3 = 14,000 ng/L
  MW 2 = 2,000
  MW 5 = 76
Wells 2, 3, and 5 have most similar signatures
Signatures onsite do not correlate well with offsite WSWs

## Slide 9: Additional Tasks Possible
  Collection of samples from raw or spent solvent, separator water, potable water prior to wet wash and/or wet wash discharge water
  Additional sample downgradient of a source area to look at potential degradation/transformation products
  Use of total oxidizable precursor (TOP) assay to look at unknown PFAS precursors that may be converted into related PFAS chemicals through oxidation – recent study shows these precursors may be high at laundry facilities

## Slide 10: Potential Actions Based on Results
  For sites where PFAS are identified at concentrations above background and EPA MCLs and NC IMACs:
    Identify locations and usage of water supply wells in the site vicinity
    Collect samples from water supply wells used for drinking water if they appear threatened and analyze using EPA Method 537.1
    Health risk evaluation (HRE) performed by DEQ toxicologist
    If alternative water supply is deemed necessary and PFAS concentrations appear potentially attributable to the dry-cleaning release, DSCA Program will provide alternative water supply and discuss with Bernard Allen Fund Program if funding available for other alternative supply
    If alternative water supply is deemed necessary and PFAS concentrations do not appear to be related to the dry-cleaning release, the DSCA Program will refer the matter to the Bernard Allen Fund Program
  If surface water bodies used as drinking water sources are threatened by PFAS contamination, surface water samples may be collected

## Slide 11: Future Implications
  Based on the results of the pilot study, the DSCA Program will evaluate if PFAS is a significant concern at dry-cleaning sites
  If PFAS is a concern, a PFAS sampling strategy will be developed for existing DSCA remediation sites
  Future PFAS sampling at DSCA sites will likely focus on water supply wells in the site vicinity
  Goal is to minimize PFAS-related expenditures where possible
  Will use existing monitoring wells to evaluate if sufficient to characterize PFAS plume
  Site closure can be pursued with PFAS impacts managed under DSCA’s current risk-based closure process

## Slide 12: Timeline
  May 2025 – site selection
  June 2025 – sampling begins
  September 2025 – sample result evaluation and application of DEQ PFAS signature tool
  November 2025 – final report on pilot study completed