## Slide 1: Per-and Poly-fluorinated Compounds Analysis Case Study: Cape Fear Drainage Basin
Mark Strynar1, James McCord2, Johnsie Lang2, Andrew Lindstrom1, Zack Hopkins3, Detlef Knappe3
1. National Exposure Research Laboratory, U.S. Environmental Protection Agency, Research Triangle Park, NC;
2. ORISE Fellow, Oak Ridge Associated Universities, Oak Ridge, TN;
3. Department of Civil, Construction, and Environmental Engineering, North Carolina State University, Raleigh, NC
LAB TECHNOLOGY DAY 2018
THURSDAY – MAY 3, 2018
MCKIMMON CENTER - RALEIGH

## Slide 3
Some Typical PFAS

## Slide 4
Rahman et al., (2014) Water Research, 50:318-340
Similar for PFOS, PFHxA and PFHxS
PFAS Generally Not Removed During Conventional Drinking Water Treatment
Notes: Work approached for detection not quantification

## Slide 5: Timeline: US EPA/NERL Water PFAS Efforts
2007 Nakayama et al., PFAS in Cape Fear Watershed
2007-2008 Decatur, AL discovery of PFAS in bio-solids, soil, surface water, groundwater
2009 (January) Provisional Health Advisory (PHA) for PFOA and PFOS established 400 and 200 ng/L
2011-2012 Sampling of Cape Fear River for determination of replacement chemistries
2012 (November) Presentation at SETAC Long Beach CA – Identification of novel polyfluorinated compounds in natural waters using accurate mass TOFMS (GenX)
2013-2014 Collaborative study with NCSU with sampling of Cape Fear River and three municipalities (Pittsboro, Fayetteville, Wilmington, NC) for legacy and PFECA determination
2014 (November) Presentation at SETAC Vancouver, BC - Determination of perfluoroalkyl ether carboxylic acids (PFECAs) and sulfonic acids (PFESAs) in North Carolina surface water using high resolution mass spectrometry (GenX and eleven other novel chemicals)
2015 (August) Publication of Strynar et al., “Identification of Novel Perfluoroalkyl Ether Carboxylic Acids (PFECAs) and Sulfonic Acids (PFESAs) in Natural Waters Using Accurate Mass Time-of-Flight Mass Spectrometry (TOFMS)” ES&T
2016 (May) OW Health Advisory for PFOS and PFOA set at 70 ng/L
2016 (November) Publication of Sun et al., “Legacy and Emerging Perfluoroalkyl Substances Are Important Drinking Water Contaminants in the Cape Fear River Watershed of North Carolina” ES&T Letters
2017 (June) Reporting of PFECAs in CFR and Wilmington drinking water – Star News Online

## Slide 6: NERL/EMMD Water Analysis Method Surface Water Ground Water WWTP Effluent Drinking Water
Also methods for:
Soil
Fish tissue
Dosed rodent tissue/fluids
Human Serum/Urine
House Dust

## Slide 7
Method Summary – Sample Processing
Nakayama et al., 2009, Strynar et al., 2015; Sun et al., 2016, Newton et al., 2017
1 L HDPE bottles
5 mL 1:1 HNO3 (35%):DI
Shipped ambient
Filter entire contents Whatman GF/A 1.7 um
Pour water out of sample bottle for volume measurement
Add filtered water back into original bottle
Subsample 500 mL
Store 500 mL
Load onto SPE tube Waters Plus style WAX
Elute for LC/MS-MS analysis
All samples Treated same way
Trip Spike
Blanks
Unknowns
Calibration
Wash bottle with 10 mL MeOH, add water back to bottle, add IS Shake

## Slide 8
performance fabrics, bio-solids, AFFF, industrial waste
Nakayama et al. 2007 ES&T 41:5271-5276
Water Sampling Cape Fear River, NC
Nakayama et al., 2007
Notes: Framed talk in terms of defining the problem
Why this is important at NERL

## Slide 9: Fact Sheet: 2010/2015 PFOA Stewardship Program
https://www.epa.gov/assessing-and-managing-chemicals-under-tsca/fact-sheet-20102015-pfoa-stewardship-program#what
Q4. What companies participated in the PFOA Stewardship Program?
Participating companies included:
  Arkema
  Asahi
  BASF Corporation
  Clariant
  Daikin
  3M/Dyneon
  DuPont
  Solvay Solexis
Q1. What is the 2010/2015 PFOA Stewardship Program?
In 2006, EPA invited eight major leading companies in the per- and polyfluoroalkyl substances (PFASs) industry to join in a global stewardship program with two goals:
To commit to achieve, no later than 2010, a 95 percent reduction, measured from a year 2000 baseline, in both facility emissions to all media of perfluorooctanoic acid (PFOA), precursor chemicals that can break down to PFOA, and related higher homologue chemicals, and product content levels of these chemicals.
To commit to working toward the elimination of these chemicals from emissions and products by 2015.

## Slide 10
Wang et al. Environment International, 2013, 60, pp 242–248

## Slide 11: OTHER PFASs: The Era of HRMS & Non-Targeted Analysis
How do we find compounds without knowing what they are?
How do we prioritize unknowns for further analysis?
How do we identify/quantify without analytical standards?
???

## Slide 12: What is Non-Targeted Analysis
Targeted Analysis
  How much PFOA is in my sample?
Suspect Screening
  Which chemicals in this database are in my sample?
  Non-Targeted Screening
  What are the chemicals in my sample?
(HRMS)
TOF
Q-TOF
Orbitrap

## Slide 13: Data Generation: Source Determination by NTA
Strynar et al. Environ. Sci. Technol., 2015, 49 (19), pp 11622–11630
Surface Water Ground Water WWTP Effluent Drinking Water
Sampling from geographically or temporally displaced locations allows triangulation of sourcing
HDPE Bottles

## Slide 14: Chromatographic and MS Data

## Slide 15: Feature Finding: Unique & Highly Different Features
Cmpd | m/z | RT | Effluent Peak Area | Upstream Peak Area
1 | 194.9263 | 0.31 | 1277673 | NA
2 | 174.9502 | 0.32 | 128095 | NA
3 | 272.9487 | 0.35 | 893478 | NA
4 | 290.9396 | 0.37 | 82068 | NA
5 | 119.0345 | 0.37 | 56430 | NA
6 | 179.0558 | 0.38 | 51910 | NA
7 | 340.9372 | 0.4 | 1961449 | NA
8 | 324.9428 | 0.41 | 75414 | NA
9 | 248.961 | 0.42 | 235520 | NA
10 | 112.9856 | 0.42 | 9963533 | NA
11 | 1033.987 | 0.43 | 185007 | NA
12 | 340.9376 | 0.49 | 847790 | NA
13 | 118.9927 | 0.5 | 242003 | NA
14 | 162.9821 | 0.5 | 1382091 | NA
15 | 1083.984 | 0.51 | 14125 | NA
Hundreds of Features of Interest
Useful For:
Identification of increasing/decreasing chemicals
Features unique to a specific location, time, treatment, etc.

## Slide 16: Relationships Reveal Underlying Chemistry
Adducts +
Fragments +
Dimers/Trimers
Homologous Series

## Slide 17: In-Source Related Species

## Slide 18: Homologous Series
+CF2
+CF2
+CF2
+CF2
Absolute Ion Intensity

## Slide 19: Isotope Signatures: Negative Mass Defect
H
F
-0.0016
+0.0078
4.8 F:H
1.00784
30.9738
14.0067
15.9949
18.9984
34.9689
78.9183
31.9721
12.0000
Positive Mass Defect
Negative Mass Defect

## Slide 20: Example of Mass Defect
Octane
MI mass 114.1409
Octanoic Acid
MI mass 144.1150
Perfluorooctanoic Acid
MI mass 413.9737

## Slide 21: Mass Defect of Outfall and Upstream Features
High Priority Species:
Unique to Downstream, Likely Fluorinated
Notes: MAKE ONE OF THESE FOR OUR DATA

## Slide 22
Fayetteville, NC (Cape Fear River)
CF 001
CF 002
CF 003
CF 004
CF 005
RC
006
CF 008,009
CF 007
Stream Flow
First Sampling 2011-2012
Presented at SETAC 2012
Follow-up sampling 2013-2013
Presented at SETAC 2014

## Slide 23
Water Intake
Current
Outfall
Former
Outfall

## Slide 24
Analyte | 001 | 002 | 003 | 004 | 005 | 006 | 007 | 008 | 008 | 009
C4 | 23 | 502 | 3761 | 6 | 4 | 0 | 8 | 7 | 5 | 3
C5 | 441 | 5607 | 43590* | 17 | 9 | 1 | 32 | 46 | 12 | 9
PFBS | 4 | 5 | 3 | 4 | 5 | 2 | 9 | 5 | 6 | 4
C6 | 17 | 90 | 434 | 18 | 12 | 2 | 27 | 16 | 18 | 14
C7 | 37 | 599 | 3873 | 14 | 17 | 0 | 11 | 20 | 21 | 9
PFHS | 7 | 12 | 10 | 9 | 7 | 4 | 9 | 10 | 9 | 22
C8 | 32 | 39 | 71 | 33 | 25 | 2 | 38 | 36 | 41 | 18
C9 | 13 | 34 | 127 | 7 | 11 | 1 | 6 | 8 | 11 | 5
PFOS | 19 | 27 | 26 | 17 | 23 | 0 | 0 | 16 | 18 | 14
C10 | 10 | 17 | 12 | 11 | 0 | 3 | 3 | 8 | 10 | 5
items in red exceed the standard curve high end of 500 ng/L; 10x diluted and re-analyzed; * still exceed curve and are estimated |  |  |  |  |  |  |  |  |  | 
Legacy PFAS found in Cape Fear Water
Stream Flow

## Slide 25
November 2015
Example Structures
Monoether (6):
GenX
polyethers (4):
Polyethers
sulfonates (2):

## Slide 26
Cape Fear River
Fayetteville to Wilmington, NC

## Slide 27
Best of ES&T Letters 2016
November 2016
June 7, 2017 story on in Wilmington Star Online News basis

## Slide 28
Pittsboro, NC
Fayetteville, NC
Wilmington, NC
Sun et al., 2017

## Slide 29
Sun et al., 2017
PFAS removal at Sweeney WTP

## Slide 30
(GenX)
Other PFECAS Sweeney WTP

## Slide 31: Chemours Site TSCA Inventory
Other
Acid Fluorides
Vinyl Ethers
Legacy
Sulfonyl Fluorides
DUPONT FAYETTEVILLE PLANT 22828 NC HIGHWAY 87 WEST FAYETTEVILLE, NC 28306-7332
http://iaspub.epa.gov/enviro/tsca.get_chem_info?v_registry_id=110000559609
CAS 697-18-7
CAS 10493-43-3
CAS 16090-14-5
CAS 677-67-8
CAS 1187-93-5
CAS 335-66-0
CAS 3825-26-1
APFO
CAS 335-67-1
PFOA
CAS 3330-14-1
CAS 1623-05-8
CAS 428-59-1
CAS 1682-78-6
CAS 2927-83-5
CAS 2062-98-8
CAS 4089-58-1
CAS 2641-34-1

## Slide 32: Hexafluoropropylene Oxide (HFPO) Based Chemistry
Vinyl Ether Production
CAS 428-59-1
HFPO-DA
In Water
NH4+
CAS 13252-13-6
CAS 62037-80-3
GenX
Common Analyte
HFPO
In water
HFPO-DAF
CAS 2062-98-8
Acid Fluorides
Polyvinyl Ether Intermediates
In Water
+Ammonium Hydroxide
Dimerized to HFPO-DAF
polymers

## Slide 33: Polyvinyl Ether Production
CAS 2062-98-8
CAS 1682-78-6
CAS 2927-83-5
CAS 10493-43-3
CAS 1187-93-5
CAS 2062-98-8
Acid Fluorides
Polyvinyl Ether Intermediates
Head-(CF2)n(CF2O)m-Head
Polyvinyl Ether

## Slide 34: Nafion Polymer
Nafion is a sulfonated tetrafluoroethylene based fluoropolymer-copolymer.
proton conductor for proton exchange membrane (PEM) fuel cells
CAS 16090-14-5
CAS 116-14-3
CAS 66796-30-3

## Slide 35: Relative Quantitation Time Trends
6 weeks mid June – early August
(HFPO-DA)

## Slide 36: Relative Quantitation Time Trends
Nafion BP2
CAS 749836-20-2
Nafion BP1
CAS 29311-67-9
6 weeks mid June – early August

## Slide 37: Retrospective HRMS Data Analysis
Samples analyzed via HRMS (TOF, QTOF, Orbitrap)
Store data files for reanalysis; like “data specimen banking”
Data Independent Acquisition when possible (QTOF) for MS/MS
Possible for presence absence analysis
Eventual sharing of data files and/or spectra to public location

## Slide 38: Mass Spectrometry Fragments
m/z
or

## Slide 39: Novel Sulfonated Fluoroethers
MS/MS
Incompatible Fragments?
Mixed Isomer?

## Slide 40: Homologous Series Improves Confirmation
Two Isomers
+CF2
+CF2
Three Isomers

## Slide 41: Unique MS/MS Fingerprints
Two Isomers

## Slide 42: Additional Polyfluoro Ether Carboxylic Acids

## Slide 43: Double Headed Fluoropolymer Intermediates
+C2F4
+C2F4
Incompatible Fragments?
Mixed Isomer?

## Slide 44: Double Headed Fluoropolymer Intermediates
+C2F4
+C2F4
Incompatible Fragments?
Mixed Isomer?
Nafion Monomer Precursor
CAS 4089-58-1

## Slide 45: Retrospective Analysis
Year | Date | 296.9473 | 346.9472 | 396.9409 | 406.9594 | 426.9657 | 340.9372 | 440.9302 | 540.9238
2011 | 11-4-11 |  |  |  |  |  |  |  | 
 | 1-26-12 |  |  |  |  |  |  |  | 
2012 | 2-1-12 |  |  |  |  |  |  |  | 
 | 2-9-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
2014 | 11-24-14 |  |  |  |  |  |  |  | 
2015 | 5-12-15 |  |  |  |  |  |  |  | 
 | 5-12-15 |  |  |  |  |  |  |  | 
 | 8-6-15 |  |  |  |  |  |  |  | 
2017 | 5-12-17 |  |  |  |  |  |  |  | 
 | 6-20-17 |  |  |  |  |  |  |  | 
 | 6-27-17 |  |  |  |  |  |  |  | 
 | 7-4-17 |  |  |  |  |  |  |  | 
 | 7-11-17 |  |  |  |  |  |  |  | 
 | 7-18-17 |  |  |  |  |  |  |  | 
 | 7-25-17 |  |  |  |  |  |  |  | 
 | 8-3-17 |  |  |  |  |  |  |  | 

## Slide 46: Retrospective Analysis
Year | Date | 296.9473 | 346.9472 | 396.9409 | 406.9594 | 426.9657 | 340.9372 | 440.9302 | 540.9238
2011 | 11-4-11 |  |  |  |  |  |  |  | 
 | 1-26-12 |  |  |  |  |  |  |  | 
2012 | 2-1-12 |  |  |  |  |  |  |  | 
 | 2-9-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
2014 | 11-24-14 |  |  |  |  |  |  |  | 
2015 | 5-12-15 |  |  |  |  |  |  |  | 
 | 5-12-15 |  |  |  |  |  |  |  | 
 | 8-6-15 |  |  |  |  |  |  |  | 
2017 | 5-12-17 |  |  |  |  |  |  |  | 
 | 6-20-17 |  |  |  |  |  |  |  | 
 | 6-27-17 |  |  |  |  |  |  |  | 
 | 7-4-17 |  |  |  |  |  |  |  | 
 | 7-11-17 |  |  |  |  |  |  |  | 
 | 7-18-17 |  |  |  |  |  |  |  | 
 | 7-25-17 |  |  |  |  |  |  |  | 
 | 8-3-17 |  |  |  |  |  |  |  | 

## Slide 47: Retrospective Analysis
Year | Date | 296.9473 | 346.9472 | 396.9409 | 406.9594 | 426.9657 | 340.9372 | 440.9302 | 540.9238
2011 | 11-4-11 |  |  |  |  |  |  |  | 
 | 1-26-12 |  |  |  |  |  |  |  | 
2012 | 2-1-12 |  |  |  |  |  |  |  | 
 | 2-9-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
 | 5-4-12 |  |  |  |  |  |  |  | 
2014 | 11-24-14 |  |  |  |  |  |  |  | 
2015 | 5-12-15 |  |  |  |  |  |  |  | 
 | 5-12-15 |  |  |  |  |  |  |  | 
 | 8-6-15 |  |  |  |  |  |  |  | 
2017 | 5-12-17 |  |  |  |  |  |  |  | 
 | 6-20-17 |  |  |  |  |  |  |  | 
 | 6-27-17 |  |  |  |  |  |  |  | 
 | 7-4-17 |  |  |  |  |  |  |  | 
 | 7-11-17 |  |  |  |  |  |  |  | 
 | 7-18-17 |  |  |  |  |  |  |  | 
 | 7-25-17 |  |  |  |  |  |  |  | 
 | 8-3-17 |  |  |  |  |  |  |  | 

## Slide 48: Questions?
Contact Information
strynar.mark@epa.gov
The views expressed in this presentation are those of the author(s) and do not necessarily represent the views or policies of the U.S. Environmental Protection Agency.