## Slide 1: Department of Environmental Quality
April 18, 2023
High Rock Lake Nutrient Strategy: Stormwater TAG

## Slide 2: Meeting Objectives for New Development Rule
Reach consensus:
  Overall rule goals
  Program jurisdiction applicability
  Local program requirements for local governments
Discuss and approach consensus:
  Development project applicability
Introduce and discuss:
  Development project stormwater requirements
Identify:
  What’s missing

## Slide 3: Agenda today, 1-3 pm
1-1:55
  Purpose of the meeting
  Reviewing agenda, ground rules & consensus
  Process updates
  Exploring nutrient-reducing Stormwater Control Measures (SCMs) and flood control
QUICK Break
2-3
  Hydrologic design to protect streams - DWR SWMM modeling project
  Considering implementation challenges
  Identifying Next Steps

## Slide 4: Ground Rules
• Stick to the tasks and topics on the agenda and keep discussion focused; one subject at a time.
• Discuss all relevant information and issues, even difficult ones.
• Keep discussion open and balanced.
• Participate, show up, share your thinking as much as you can.
• Strive to make decisions by consensus.
• Look beyond positions to interests.
• Disagree openly and respectfully.
• Put personal differences aside in the interests of a successful team.
• Jointly design ways of testing disagreements and look for mutually beneficial solutions. • Follow through on commitments.
• Share information discussed in team meetings with your organization and reflect its position back to the team.
• While participants are free to discuss the process outside of official meetings, decisions will be made during meetings themselves.

## Slide 5: Decision-Making Process re: consensus
From High Rock Stakeholder Engagement Process Charter, p. 11
“Consensus requires the active participation of everyone in the group and an atmosphere where disagreements are respected. When someone disagrees, the goal of the group shall be to discover the reason for the objection and to find a way to work toward meeting that need in a revised agreement. Consensus is being defined as at a minimum, “I can live with and support the decision.”
“Consensus agreements reached in one team meeting should not be reconsidered in a subsequent meeting without the consent of all participants in attendance.”

## Slide 6: Updates & Action Items
Scott Leonard will share a map of the Davidson County watershed district with the group
Kelsie and Justin will identify the original start date for post-construction stormwater control permitting in High Point
TAG members will consider what other communities are developing zoning restrictions specifically to manage stormwater/flooding
Danica asked if it would be possible to identify how many poor or fair SCMs (i.e. dry detentions) exist in the watershed which could be retrofitted
Tetra Tech’s watershed model report has been uploaded to ShareFile
Consultants Update…

## Slide 7: Stormwater Control Concerns
Nutrient loading rate targets applied at a BUA (impervious cover) threshold greater than 10% don’t protect streams from becoming nutrient sources
Detention and multi-day discharge does not protect streams from becoming nutrient sources
Wet pond detention is easy and requires relatively little space, but provides limited nutrient treatment, prolongs erosive flow, and can create algal toxicity risks
Infiltration is needed, but takes up lots of space, is difficult, expensive, and prone to failure
Slow filtered discharge can serve the same purpose, but with smaller footprint
Undersized infiltration practices can outperform properly sized wet ponds
“Water Quality Volume” ideally captures and treats of 90% of annual storm events (i.e. 90th percentile storm
  1” is actually about 80% in piedmont (i.e. 80th percentile storm)
Existing green footprint (medians, gardens, open space) can be used to aid infiltration
Existing development is already creating the problem, New D rules must keep things from getting worse

## Slide 8: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 9: SWMM Modeling
Objectives: Study hydrologic control options that better protect receiving streams
Study basics:
  Use multi-decade historical rainfall record + climate change projections
  Evaluate range of development scenarios/intensities
  Test alternative SCM designs for hydrologic capture and fate
  Identify alternative SCM designs to expand runoff reduction toolbox
Storm sizes being considered:
  1yr/24hr
  90th percentile
  1” rain event
Runoff reduction options:
  Low end: conventional treatment of 90th percentile storm event
  High end: annual runoff volume match
Desired product:
  Achievable design requirements that provide better stream protection

## Slide 10: Applicability Thresholds
Possible Approaches
Land disturbance
  Erosion and Sediment Control program uses 1 ac
  Falls Lake NMS rules use 0.5 ac residential, 0.25 ac commercial
Impervious cover (BUA) percentage
  Challenging to define “project area” for certain types of development (i.e. an entire community college campus or each individual building)
Impervious cover (BUA) total square footage
  Simple to calculate and assess
Proposed exemption
Single Family Individual Lot w/ <5% BUA
  supersedes disturbance threshold
Minimum requirements to run SNAP Tool

## Slide 11: Water Supply Watershed Program (NC)
Zoning Designations | NC Impervious Cover% (BUA) | Lot Size | Connecticut Impervious Cover %
 | 6% | 2 ac | 8%
RS-40 (Winston-Salem) | 12% | 1 ac | 12%
RS-20 (Winston-Salem) | 24% | 0.5 ac | 19%
RS-12 (Winston-Salem) |  | 0.25 ac | 25%
RS-7 (Winston-Salem) |  | 0.15 ac | 38%

## Slide 12: Example Applicability Criteria
Development resulting in the disturbance of at least 1 acre of land
Residential development consisting of 5 or more dwelling units
Residential development of fewer than 5 dwelling units involving construction of a new or reconstructed road
Residential development of fewer than 5 dwelling units where impervious cover after construction exceeds 30%
Stormwater discharge to wetlands/watercourses
Land uses or activities with potential for higher pollutant loadings
Industrial/commercial development which results in 10,000 sqft of impervious surface
New highway, road, and street construction
Modifications to existing storm drainage systems
State of Connecticut

## Slide 13: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 14: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 15: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 16: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 17: Rule Content Framework and Options
Goal Options:
  Meet strategy % reduction goals on project basis
  No net nutrient loading increase from pre-development, protect receiving streams
Program applicability:
  All local governments
  Only local governments showing certain growth levels
    Adds flexibility for areas with little or no growth
Local program requirements:
  Post-construction treatment (SWMM Modeling, see next slide); ongoing SCM maintenance; ensure project compliance for life
  Education; mapping; illicit discharge detection and elimination (propose moving to Existing Development rule)
Project applicability:
  Disturbance thresholds (see next slides)
  Exempt - Individual single family residential lot development <5% BUA
  Exempt - Existing development, redevelopment regulated per statute, agriculture rule activities
Project requirements (current Neuse/Tar-Pamlico):
  Meet unit-area loading rate target OR do annual runoff volume match
  24% BUA treatment threshold, 1” design storm, primary SCM; offset option allowed for remainder
    Lowered BUA threshold for treatment, larger design storm (SWMM Modeling)
    Reduced treatment requirements for lower density, no treatment requirements for very low density
  Road-only or sidewalk-only projects can do entirely offset

## Slide 18: Questions?
Department of Environmental Quality
Joey Hester
Joey.hester@ncdenr.gov
O: 919-707-3675
C: 919-418-5712