## Slide 1: Department of Environmental Quality
November 6, 2023
High Rock Lake Nutrient Strategy: Stormwater TAG

## Slide 2: Meeting Objective for Existing Development Rule
TAG members share feedback on proposed refinements to tiered post-construction stormwater requirements

## Slide 3: Agenda today, 1-3 pm
1-1:30
  Purpose of the meeting
  Reviewing agenda, ground rules & consensus
  Review TAG status
1:30-2:50
  Present and discuss revised stormwater tiered concept
2:50-3:00
  Identifying Next Steps

## Slide 4: Stormwater TAG Status
Consensus decisions made:
  New D Stormwater Rule will include all local jurisdictions
  Support for a funding-based compliance mandate for Existing Development Stormwater Rule
SWMM Modeling
HRL Rulemaking Considerations
  New D rule will move forward, may be informed by SWMM modeling (rule readoption expected at 10-years)
  Alternative stormwater objective:
    Older rules called for loading rate targets
    Proposing neutralization of nutrient load increases & hydrologic protection

## Slide 5: Tiered Post-Construction Stormwater Requirements
 |  | No curb & gutter within proposed development, including new proposed roads | Curb & gutter included in proposed development
BUA < 6% |  | Vegetated conveyances only Disconnect impervious cover from conveyances Disperse IC-concentrated flows | Not applicable
6% ≤ BUA < 12% |  | Vegetated conveyances only Disconnect impervious cover from conveyances Disperse IC-concentrated flows Treat transportation impervious cover w/ primary SCM or runoff-reducing secondary SCM | Treat site runoff from 1" w/ primary SCM, including volume reduction requirement (see below), calculated w/ curve number method OR Treat site runoff from 90th percentile storm w/ primary SCM
12% ≤ BUA | Stream Protection Criteria | Potential Options for Initial Discussion Control the 2yr/24hr post-development peak flow rate to 50% of the 2yr/24hr pre-development level OR Control the 2yr/24hr post-development peak flow rate to the 1yr/24hr predevelopment level OR Detain the volume difference between the post-development 24-hour storm and the pre-development 24-hour storm, releasing the volume over 24 hours | 
 | Water Quality Treatment Criteria | Treat site runoff from 1" w/ primary SCM, including volume reduction requirement (see below), calculated w/ curve number method OR Treat site runoff from 90th percentile storm w/ primary SCM | 

## Slide 6: Definitions/Requirements
Transportation Impervious Cover: Uncovered, paved or hardened surfaces used by vehicles, including parking areas, driveways, and roads
Primary SCMs: Bioretention, Infiltration, SW Wetland, Permeable Pavement, Wet Pond, Sand Filter, Rainwater Harvesting, StormFilter, Silva Cell, others specified in NC Stormwater Design Manual
Runoff-reducing Secondary SCMs: DIS; LS-FS; Treatment Swale
Volume Reduction Requirement (SCS method)
Portion of 1" of runoff that is required to be achieved via evapotranspiration, infiltration, or slow filtered discharge
Stream Protection Criteria Exemptions
  The entire channel protection volume is recharged to groundwater
  Sites less than or equal to one acre of impervious cover
  Compliance with the stream protection criteria above can be demonstrated to result in no benefit to current and future downstream development
Hydrologic Soil Group | Volume Reduction Requirement
A | 0.38
B | 0.26
C | 0.13
D | 0.07

## Slide 7: Next Meeting
November 28
  Expecting to finalize recommendation for post-construction stormwater treatment
  Proposal forms basis for initial recommendation, provisions not set in stone
Final report to Steering Committee (tentatively December)
  Includes consensus decisions, split decisions, non-regulatory recommendations
  Steering Committee expected to approve with additional comment/analysis
  Steering Committee final report expected in January
Rule drafting expected through summer 2024, then phase II of stakeholder feedback
Potential Dates

## Slide 8: Questions?
Department of Environmental Quality
Joey Hester
Joey.hester@ncdenr.gov
O: 919-707-3675
C: 919-418-5712