## Slide 1: Riparian Buffers for Water Resource Protection
Michael R. Burchell II
Professor and Extension Specialist
Department of Biological and Agricultural Engineering
NC State University

## Slide 2
Riparian Areas
From Latin ripa – area adjacent to a watercourse
In NC most of the floodplains were well vegetated – mostly forested
Considered an ecotone
  Transitional area from upland to aquatic
  Like a cell membrane controlling how materials enter the stream
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 3
Riparian Buffers
Vegetated streamside corridors (either protected or restored) meant to protect stream ecological functions and downstream water quality
Example mid-western buffer
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 4
Riparian Buffers
25 years ago, buffer experts (national and NC State) plus state officials joined to determine realistic buffer width to minimize land to put into buffers
Result = minimum 50 feet, two zone buffer (grass + trees)
NRCS ideal buffer design to achieve multiple functions
Floodplain
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 5
Riparian Buffers
Research has shown buffers can provide 4 functions
http://www.mda.state.mn.us/protecting/conservation/practices/bufferforested.aspx
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 6
1. Protect Stream Structure
Vegetation within the buffer slows surface water down
Roots near stream stabilize banks (particularly in bends)
Slower runoff + reinforced streambanks = less erosion
Less streambank erosion = less sediment loss downstream
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 7
2. Enhance Aquatic Environment
Tree canopy provides shade
  Temperature control
  Higher oxygen
  Controls algae
Leaf litter
  Carbon and organic nutrients (energy for food web)
  Habitat
Coarse woody debris
  Habitat
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 8
Temperature – Forested Riparian Areas
Lloyd Swift, US Forest Service Coweeta Hydrologic Laboratory – 135 ac clearcut in mixed hardwood forest, 40 ft wide riparian buffer, N-S oriented first order stream, Pisgah National Forest near Brevard, NC
Effects of Clearcut Timber Harvesting on stream temperature
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 9
3. Reduce Sediment and Phosphorus from Surface Runoff
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 10
3. Reduce Sediment and Phosphorus from Surface Runoff
Surface runoff
Grass filter slows water
Encourages diffuse flow (critical component)
Sediment and sediment –bound P is deposited
Sediment can be trapped, P uptake by vegetation possible
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 11
From: NCSU Technical Bulletin 318 - Riparian Buffers and Controlled Drainage to Reduce Agricultural NPS Pollution. From D. Osmond with permission.
Sediment reduction can be high
3. Reduce Sediment and Phosphorus from Surface Runoff
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 12
Other Analysis on Sediment
Liu et al. (2008) at 85 sites
  30 ft buffer – 85% removal
  50 ft buffer – 94% removal
  100 ft buffer – 100% removal
  Possible over-prediction due to experimental setup?
Sweeny and Newbold (2014) at 22 sites
  30 ft buffer – 64% removal
  50 ft buffer – 74% removal
  100 ft buffer – 80% removal
Note – sediment that is lost has more fine particles and will be more easily transported downstream
Other analysis on sediment - Predictive Models
3. Reduce Sediment and Phosphorus from Surface Runoff
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 13
Sediment-attached Phosphorus removal can follow similar trends
3. Reduce Sediment and Phosphorus from Surface Runoff
% P remaining
From: NCSU Technical Bulletin 323 – North Carolina Phosphorus Loss Assessment. From D. Osmond with permission
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 14
4. Reduce Nitrate-Nitrogen from Groundwater before it Discharges to the Stream
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 15
Riparian Buffers – Nitrogen removal
Buffers can be effective sinks of NO3 through
Microbial denitrification
Plant uptake
Shallow Ground Water Flow
Restrictive Layer (Aquitard)
Aerobic Soil
Anaerobic or Hydric soils
NO3
NO3
NO3
NO3
NO3
NO3
NH4 NO3
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 16
Riparian Buffers – Nitrogen removal
Areas in the floodplain have:
High plant productivity
High soil carbon
Shallow Ground Water Flow
Restrictive Layer (Aquitard)
Aerobic Soil
Anaerobic or Hydric soils
NO3
NO3
NO3
NO3
NO3
NO3
NH4 NO3
Groundwater close to the surface
Low soil oxygen
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 17
Riparian Buffers – Nitrogen removal
This leads to higher plant uptake of NO3
In the absence of oxygen, soil microbes use NO3 instead (denitrification) and release N2 to the atmosphere
Both processes combine for significant potential removal of N
Groundwater Flow
NO3
N2
Denitrification
“hot spot”
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 18
Other Analysis on Nitrogen Removal
Mayer et al. 2007 at 88 sites
Buffer width in feet
Note: Surface + subsurface contributions
<80
<80-160
160+
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 19
Riparian Buffers
Aerobic Soil
Anaerobic or Hydric soils
Wells
Grass Pines Hardwoods
NC studies on buffers enrolled in the NC CREP Program
Tar-Pamlico Basin
2-5 years data
54-72 groundwater wells per site across experimental blocks
Typical experimental setup
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 20
Site 1
NO3 -N Source - Cropland
Section 1 (200 ft width)
- Groundwater at Field Edge
4 mg/L NO3-N
- Higher Elevation
Section 2 (150 ft width)
- Groundwater at Field Edge
12 mg/L NO3-N
- Lower Elevation
- Wetland indicators
Shallow– 89% reduction
Deep – 54% reduction
Shallow– 63% reduction
Deep – 15% reduction
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 21
Site 2
Stream Flow
Water Table Well
Water Quality Well: Shallow and Deep
Redox Probe Nest: Shallow and Deep
Groundwater Flow Direction
Zone 1
Existing Hardwood Buffer
Zone 2-Pine Conservation Buffer)
Zone 3 (Grassed)
Cropland
NO3 -N Source – Cropland
3 Blocks (390 ft width)
Zone 1 Existing Hardwood Buffer
– “A misunderstood paper”
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 22
Site 2 – Elevation Cross Section
Floodplain
Limited Nitrate
removal
20-80% removal
in floodplain
390 328 263 197 131 65 0 -65
Distance from stream (ft)
Approx. 4 ft elevation drop
New pines
  Treatment DID OCCUR in the existing hardwood forest within the floodplain within the last 65-75 feet to the stream
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 23
Conclusions
Riparian Buffers can:
  Protect stream structure
  Enhance the aquatic environment
  Reduce sediment and phosphorus form surface runoff
  Reduce nitrate-nitrogen from groundwater before it discharges to the stream
Often, riparian buffers will provide most of these important functions at all sites
Research strongly supports the fact that buffers are a critical component of successful water quality protection strategy in NC watersheds
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 24
Conclusions
Overall, research indicates most buffer functions approach a maximum at or above 100 feet and start to diminish at different rates as buffers widths get more narrow
Buffers less than the 50 ft width requirement could significantly reduce the effectiveness in N removal (less treatment area) and sediment removal (particularly on lands with higher slopes).
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues

## Slide 25
Thank you!
mike_burchell@ncsu.edu
Notes: Impacts on natural resources
Algal over production
Environmental, Social, and Economic Issues