## Slide 1: Department of Environmental Quality
January 26, 2023
High Rock Lake
Nutrient Management
Strategy: Stormwater

## Slide 2: NMS Rulemaking
Engage stakeholders in watershed planning
Prioritize and enable creative and innovative solutions that meet the needs of residents
Eliminate chlorophyll-a impairment and restore full uses of the Lake (fishing, swimming, recreation)
Protect drinking water supplies along the Yadkin River and around High Rock Lake
Implementation Outcomes
Department of Environmental Quality

## Slide 3: Stakeholder Engagement
Engage stakeholders in watershed planning
Prioritize and enable creative and innovative solutions that meet the needs of residents
Document existing stormwater management regulatory landscape in HRL
Draft conceptual proposals for
  Reducing nitrogen and phosphorus loading from developed lands
  Implementation timelines
  Adaptive management
Identify regulatory and administrative barriers to implementation
Combine conceptual proposals into a formal recommendation for DWR staff
Process Goals

## Slide 4: HRL Chlorophyll-a Impairments
2018 2020 2022

## Slide 5: State and Federal Statutes
Clean Water Act
  Set water quality parameter standards to protect “uses” (recreation, drinking water, fishing, etc.)
  When WQ parameters are exceeded, designate a water body “impaired”
  Develop a restoration/remediation plan to reduce inputs to comply with WQ standards
  Monitor implementation until WQ standards are met
  Eliminate the impairment and recover full uses of water body
§ 143-215.8B
  Regulate point and nonpoint sources of pollutants
  Establish nutrient reduction goals
§ 143B-282
  EMC adopts rules to assure water quality standards are met
  Address point and nonpoint sources of pollutants
15A NCAC 02B .0211
  Sets chlorophyll-a standard and requires EMC to regulate contributing sources
Regulatory Obligations

## Slide 6: Rulemaking Timeline
Chart: High Rock Lake DRAFT Rule Development Timeline
| Draft Strategy Framework | Stakeholder Engagement Phase I | Draft Rule Language | Stakeholder Engagement Phase II | Rulemaking Approval | Public Comment Period | Final Approval
Start Date | 44440 | 44833 | 45078 | 45231 | 45352 | 45536 | 45717
Duration | 393 | 244 | 152 | 119 | 183 | 180 | 245

## Slide 7: High Rock Lake Watershed Annual Nutrient Loading
Department of Environmental Quality
Source: Tetra Tech 2012

## Slide 8: Nutrient Load “Reductions”
Department of Environmental Quality
Source: Tetra Tech 2012

## Slide 9: Department of Environmental Quality
January 26, 2023
High Rock Lake
Nutrient Management
Strategy: Baseline Data

## Slide 10: High Rock Lake Watershed Annual Nutrient Loading (tons/yr)
Department of Environmental Quality
Chart: Urban Loading
| Yadkin River | South Yadkin River | Grants Creek | Abbotts Creek | Flat Swamp Creek | Dutch Second Creek | Town/Crane Creek | Swearing Creek | North & South Potts Creek
Source N | 718.2127 | 272.752 | 30.5891 | 80.7228 | 7.6593 | 17.8942 | 21.5328 | 12.9395 | 11.1734
Delivered N | 450.3899 | 166.313 | 23.2469 | 40.6035 | 6.4327 | 14.9387 | 16.8973 | 10.2037 | 9.2848
Source P | 93.6442 | 37.3317 | 3.3023 | 7.5769 | 0.70434 | 1.8163 | 2.1857 | 1.1899 | 1.0544
Delivered P | 55.8371 | 19.6092 | 2.6896 | 3.7023 | 0.6011 | 1.4724 | 1.8876 | 0.94738 | 0.8552
Chart: MS4 Loading (boundaries as of 2012)
| Yadkin River | South Yadkin River | Grants Creek | Abbotts Creek | Flat Swamp Creek | Dutch Second Creek | Town/Crane Creek | Swearing Creek | North & South Potts Creek
Source N | 317.9728 | 63.4287 | 29.3812 | 75.7851 | 0 | 0 | 18.2804 | 19.0248 | 1.66
Delivered N | 205.8836 | 38.8307 | 24.0064 | 45.3061 | 0 | 0 | 14.3451 | 15.0024 | 1.3794
Source P | 31.0426 | 7.8218 | 2.705 | 6.1354 | 0 | 0 | 1.6366 | 1.5461 | 0.13491
Delivered P | 22.9183 | 4.2552 | 2.3482 | 4.0367 | 0 | 0 | 1.4134 | 1.231 | 0.10942
Urban: CGIA “developed” outside of MS4 boundaries

## Slide 12: Nutrient Load Reductions
Curve determines overall % load reduction needed
% load reduction applied to nutrient export rate which determines SCM type & size

## Slide 13: Current NC Stormwater Regulations in HRL
NPDES MS4 (14 in HRL)
  Construction site and post-construction stormwater controls
    All projects: 30’ setback
    Low density: dispersed flow, vegetated conveyances
    High density (> 24% BUA): treat 1” BUA runoff w/primary SCM; or annual runoff volume match
  Public education
  Illicit discharge elimination
  Pollution prevention & “good housekeeping”
HQW/ORW/WSW
  30’ vegetated setback
  Low density = dispersed flow, vegetated conveyances
  High density (varies from 6% to 24% BUA): treat 1” BUA runoff w/primary SCM; or annual runoff volume match, 100’ vegetated setback

## Slide 16: Overview
Model program approved by EMC, local programs required
2 approaches to local governments included - N/T = “Swiss cheese”; J/F = all LGs
Programs include post-construction control, AND some or all of:
  ensure compliance, SCM maintenance for life of development;
  public education;
  mapping stormwater system;
  illegal discharges detection/elimination program.
Post-construction stormwater requirements:
  All use nutrient loading rate targets (lb/ac/yr); meet strategy goals project by project
  Onsite-offsite practices combine to meet targets
  Onsite
    Quality: Treatment minimums vary by rule; 30-50% of reduction need (Falls) or one primary SCM (others)
    Quantity: peak rate match, 1 yr/ 24 hr storm (Falls only)
  Offsite – buy credit for remaining load reduction per Nutrient Offset Rule 15A NCAC 2B .0703
    Private offset bank via DWR - https://deq.nc.gov/about/divisions/water-resources/water-quality-permitting/401-buffer-permitting/nutrient-offset-buffer-mitigation-program
    No bank credits available? DMS - https://deq.nc.gov/about/divisions/mitigation-services/customers/nutrient-offset-ilf-program-information
New Development Nutrient Stormwater Rules

## Slide 17: Details
Neuse: 3.6 lb N/ac/yr loading rate target (or volume match);
Tar-Pamlico: 4.0 lb N/ac/yr, 0.4 lb P/ac/yr (or volume match);
Both Neuse and Tar (readopted):
  > 24% BUA 1o SCM; offset remainder
  Disturbance thresholds: 1 ac residential; ½ ac commercial/industrial/multi-family
  Exemption for individual SF lots NPOLCPDOS w/ <5% BUA
Falls:
    Disturbance thresholds: ½ acre residential; 12,000 ft2 commercial/industrial/multi-family
    2.2 lb N/ac/yr, 0.33 lb P/ac/yr (or volume match)
    Meet 30-50% of load reduction need onsite; offset remainder
Jordan:
  Nitrogen: UNH 2.2; LNH 4.4; Haw 3.8 lb/ac/yr
  Phosphorus: UNH 0.82; LNH 0.78; Haw 1.43 lb/ac/yr
  All projects above targets > 1 BMP, 85% TSS.
  Offset remainder where < 10 lb N/ac comm./ind. or < 6 lb N/ac SF residential
    Delivery factors apply, offset based on lake-delivered loads
  Quantity: peak rate match, 1 yr/ 24 hr storm
New Development Nutrient Stormwater Rules

## Slide 18: Stormwater Nitrogen and Phosphorus (SNAP) Accounting Tool
Currently used in Falls (Neuse, Tar-Pamlico begin using 2023)
Designed for usability across the State
Spreadsheet calculation, annual nitrogen and phosphorus runoff export from a development site with or w/o treatment (lb/ac/yr)
  Annual runoff volume * landcover-specific nutrient concentrations
  Annual runoff volume calculated with Simple Method
  Models nutrient reductions by Stormwater Control Measures (SCMs)
SCM nutrient treatment
  Inflow = catchment land covers area-weighted aggregate concentration
  Inflow partitioned through SCM to hydrologic fates
  Effluent - fixed event mean concentrations, SCM-specific
Site aggregated into annual runoff load N and P (lb/ac/yr)

## Slide 19: From DEMLR SCM Credit Doc

## Slide 20: Overview (cont’d) – Jordan, Falls
Regulated parties = all local governments
Jordan:
  Stage 1: Education, mapping, IDDE, Retrofits ID
  Stage 2 @ 5, 7 years: Lake monitoring trigger – Impaired? -> Programs required
Jordan, Falls: Nutrient load reduction programs
  Reduction targets = strategy goals applied to pre-New D developed lands w/in jurisdiction
    Falls Stage 1 target = offset post-baseline difference
  Propose pace of implementation – negotiable
    except Falls Stage 1 = 10 ~16 yrs
    Falls – Association alternative plan, “IAIA” = spending-based pace
  Broad latitude on load-reducing practices
    Main focus = existing developed lands w/in jurisdiction; challenging
    May also obtain reductions from other sources
    Joint compliance, combined (rules) compliance options
    (Initially) Only practices with approved nutrient crediting
    (Later) Falls IAIA: Explicit list – includes nutrient-friendly practices lacking accounting
Existing Development Stormwater Rules

## Slide 21: Lessons Learned
New Development
  Avoidance
    Development “leaks” outside of regulated areas
    Local governments zone to avoid high density, or developers build to 23.9% BUA
    Whereas studies find stream degradation begins ~10% watershed BUA. Streambanks become nutrient source
  Standardization of req’s across watershed preferable to minimize sprawl, leakage
    However, recognize local administrative capacity is variable; need assistance options
  Lower density thresholds are appropriate
  Evidence suggests streams degrade under runoff from 1” treatment regime
Existing Development
  Reduction opportunities on existing developed lands challenging, costly; need to expand options
  Nutrient credit not yet established for many useful practices; need to loosen constraints
  Load reduction needs estimation challenging, draws over-focus, value/effort questionable; need to de-emphasize as compliance metric
  Progress clearly a long-haul proposition; needs to be built into recurring admin responsibilities

## Slide 22: Questions?
Department of Environmental Quality
Joey Hester
Joey.hester@ncdenr.gov
O: 919-707-3675
C: 919-418-5712

## Slide 23: New Development Rule Considerations
Nutrient export rate calculations, credits
Density thresholds
Primary vs Secondary SCMs
Hydrologic soil groups