## Slide 1: August 16, 2023
Water Supply Watershed Protection Program
Paul Clark, Division of Energy, Mineral and Land Resources

## Slide 2: Water Supply Watershed Protection (WSWP) Program
Purpose: Protect NC’s Surface Water Drinking Supplies
Department of Environmental Quality

## Slide 3: WSWP Program Requirements 15A NCAC 02B .0624
Department of Environmental Quality
Minimize volume of stormwater runoff.
Minimize pollutant load of stormwater runoff.
Limit built-upon area (impervious cover)
Vegetative setbacks (buffers)
Stormwater controls
Certain prohibitions (Allowed/Not Allowed Uses/Activities)

## Slide 4: History
1989-2023 | Voluntary Programs
1989 | Water Supply Watershed Protection Act ratified
1992 | Rules adopted and surface waters reclassified
1993-94 | Local governments implement WSWP program
1995 | Rules revised, model ordinance developed
2012 | General Statute (included density averaging) passes
2019 | Rules revised
2021-2023 | Model ordinance revised
Notes: There were other statute changes during this time. Only 2012 mentioned because DA added.

## Slide 5: WS Surface Water Classifications
Primary
  Class C: general purpose
  Class B: primary recreation
  WS-I thru WS-V: water supply
Supplemental
  HQW, ORW, TR, NSW
Notes: Stream assessments determine uses which determine classifications which then determine standards. Local government WSWP ordinances and watershed maps shall be submitted to DEMLR for approval by Commission by Division (or designee – DEMLR) no later than 270 days after receiving notice of water supply reclassification by EMC.

## Slide 6: Water Supply Reservoirs
Balance of Watershed
(WSII, WSIII)
or 5 miles Protected Area (WS-IV)
Critical Area
1/2 mile
Water Supply Intake
Reservoir
Notes: No critical area in a WS-I since they are essentially undeveloped.
Critical area of a reservoir is ½ mile from normal pool elevation.
Close-up example of a typical water supply watered – a reservoir. Each ws/ws has two distinct areas: CA and PA or BW.

## Slide 7: Run of River Water Supplies
Balance of Watershed
(WSII, WSIII)
Or 10 miles
Protected Area (WS-IV)
Critical Area
1/2 mile
Water Supply Intake
Notes: Protected area in a WS-IV is measured as 10 miles upstream and draining to intake (measured run-of-the-river)
Natural stream or river – critical area is ½ mile upstream and draining to intake

## Slide 8: WSWP Program Delegated Local Authority
82 Counties
209 Municipalities
(1 coordinator)

292 WSWP Programs (potential)
1 Airport Authority
292-52 = 240 programs (actual)

## Slide 9
WSWP Program Implementation
Local Government Responsibilities
Watershed protection ordinance
Develop/maintain maps (state vs. local)
Review projects for compliance (tracking systems)
Interlocal agreements (when used)
Recordkeeping and reporting
Maintenance of SCMs
Variances
Notes: State map based on classification. Local map has to be at least as stringent, but can be larger to follow property lines, roads, etc. Watershed map boundaries can be revised upon request.
IAs – county administers program for state, 10/70 transfer

## Slide 10: Allowed/Not Allowed

## Slide 11: Reviewing Projects - Development Main Criteria
Density/Built Upon Area
Vegetated Setbacks
Stormwater Control

## Slide 12: Reviewing Projects - Development Site Plans Include:
Department of Environmental Quality
  Surface waters
  Vegetated setback boundaries
  Impervious cover
      roads/sidewalks
      building locations
  Lot lines
  Stormwater flow/drainage
  Stormwater Control Measures (when applicable)
  Calculations
      Stormwater
      BUA, etc

## Slide 13: Allowable BUA Limits
Class | Low | High
WS-I | Public, undev. | 
WS-II CA | 6% | 24%
BW | 12% | 30%
WS-III CA | 12% | 30%
BW | 24% | 50%
WS-IV CA | 24% | 50%
PA | 24% (36%) | 70%
WS-V | No restrictions | 
Notes: No critical area in a WS-I since they are essentially undeveloped.
Critical area of a reservoir is ½ mile from normal pool elevation.
Close-up example of a typical water supply watered – a reservoir. Each ws/ws has two distinct areas: CA and PA or BW.

## Slide 14: Density/BUA Calculations:
Department of Environmental Quality
Impervious surfaces include:
  Building footprints
  Parking lots
  Most graveled surfaces
  Courts (except grass courts)
  Driveways and sidewalks
  Definition (NCGS 143-214.7)

## Slide 15: Vegetated Setbacks
Low density:
30’ from perennial stream
High density:
100’ from perennial stream
No new BUA allowed in vegetated setback
SCMs (although not specifically prohibited)
should generally not be placed in vegetated setbacks – ACOE requirements

## Slide 16: Stormwater Control
Department of Environmental Quality
Low Density:
Preferred - vegetated conveyance
Alternate-curb/gutter outlets to vegetated swales or other areas
High Density:
Engineered SCMs meet MDC
Runoff treatment or runoff volume match

## Slide 17: Definitions
Runoff Treatment: sw runoff volume generated from project BUA at build-out during storm of required storm depth treated in one or more primary SCMs or combination of primary and secondary SCMs provide equal or better treatment
Runoff Volume Match: annual runoff volume after development shall not be more than ten percent higher than annual runoff volume before development (exception-SA-five percent)

## Slide 18: Special Provisions
Department of Environmental Quality
10/70 Option: new development up to 70% BUA in 10% of watershed within jurisdiction
Density Averaging: development plans for up to two noncontiguous parcels (at one time) to be submitted together as single project
Cluster Development: modified lot sizes and setback distances to conserve naturally-sensitive land

## Slide 19: Survey
46 Questions
Option to upload digital copies or ordinance(s) and map(s)
Sent to ~292 local governments who administer WSWP programs
47 Percent Responded (Aug 2023)
Survey link

## Slide 20: Survey Purpose
Department of Environmental Quality
  State to learn more about local programs
  Local governments to seek guidance from state
  State to prioritize local governments for program review/audit

## Slide 21: Updated, Revised Draft Model Ordinance
Why revise/update model ordinance?
  Last revised 1995
  Incorporate statute and rule changes
  Improve clarity and ability to use

## Slide 22: Updated, Revised, Draft Model Ordinance
Department of Environmental Quality
Table of Contents
ARTICLE 100 DEFINITIONS
ARTICLE 200 AUTHORITY AND GENERAL REGULATIONS
ARTICLE 300 SUBDIVISION REGULATIONS
ARTICLE 400: DEVELOPMENT REGULATIONS
ARTICLE 500: PUBLIC HEALTH REGULATIONS
ARTICLE 600 ADMINISTRATION, ENFORCEMENT AND APPEALS

## Slide 23: Summary of Changes from 1995 to 2023 Ordinances
Content Changes
  Article 100 - some definitions added and some changed to improve clarity
  Articles 200 and 300 – minor changes to improve clarity
  Article 400
    Allowed/Not Allowed Use table added to improve presentation and clarity of information.
    Density and Built Upon Area table is taken almost directly from regulations and improves presentation and clarity of information.
    Density Averaging section added to incorporate 2012 NCGS change
  Articles 500 and 600 – minor changes to improve clarity
Organizational Changes
  Definitions section moved from end to beginning of document
  Footnotes consolidated and moved to end of document.
WSWP page includes ordinance link

## Slide 24: Ordinance Update/Revision Timeline
Department of Environmental Quality
Initial draft prepared and shared with small group
Small group comments received and draft revised
Draft revised
  Shared with all WSWP local governments
  Shared with other listservs (i.e., stormwater, etc)
  Posted on WSWP website
  Comments due May 28, 2021
July 7, 2021 - EMC-WQC approves updated, revised draft model ordinance
September 9, 2021 - NCDEQ seeks full EMC approval – EMC requests that draft be revised by those with local ordinance expertise (UNC-SOG).
2021-2023 – NCDEQ seeks/receives additional comments on revised/updated draft model ordinance and revises ordinance (Richard Whisnant and Jim Joyce).
March 9, 2023 - EMC approves ordinance

## Slide 25: Some FAQs
Department of Environmental Quality
Have the Appendices from 1995 model ordinance been updated revised?
  Appendices A, B, and C have not been updated or revised.
  Appendix C may be updated/revised first because it includes information on financial assurances and some other items on which I’ve rec’d some questions.
Do local governments have to include certain sections in their ordinances?
  Model ordinance is a guide, it does not have to be followed exactly, but
  Local governments often include the main components of the WSWP program, but model specifics are local government decision.
Do local governments have to offer financial assurances such as performance bonds, etc.?
  There is nothing in statute or regulations that require financial assurances.
  This decision is up to the local government.
Do programs have to offer Density Averaging?
  Yes
Can a program offer Low and High Density and 10/70 option?
  Yes
Can a program offer only Low Density?
  Yes

## Slide 26: Some FAQs (continued)
Department of Environmental Quality
What records need to be maintained and which of those need to be sent to state.
  a copy of all variance requests and associated documents;
  findings of fact on all variance requests;
  a description of all projects for which the local government has granted a variance to the requirements of Rules .0621-.0624 of this Section;
  an accounting of projects approved under the local government's 10/70 Option (as described in Rule .0624 of this Section), as applicable; and
  records of inspections of SCMs

## Slide 27: Some FAQs (continued)
Department of Environmental Quality
What about Criminal Liability?
  Prohibition on criminal penalties for certain ordinance violations in SL 2021-138, Part XIII is not clear regarding ordinance that may have multiple sources of authority. Water Quality protection rules are primarily drawn from Chapter 143, so one could interpret this rule to allow criminal penalties for violation of water supply watershed regulations. It is unclear how and whether SL 2021-138 applies to water supply wateshed protection ordinances
  The above paragraph will be added as a footnote in the next version of the ordinance.

## Slide 28: WSWP Webpage and Contact Info
Paul Clark
  (paul.clark@ncdenr.gov)
  919-707-3642
https://deq.nc.gov/about/divisions/energy-mineral-and-land-resources/stormwater/stormwater-program/water-supply-watershed-program